## Slide 2
Introduction to Warheads
Aim: To understand the scientific principles associated with warhead design.
Learning Outcomes: Upon the successful completion of this module, the student should be able to:
Understand basic warhead components, factors affecting their performance, the lethal mechanisms that may be selected and why; and
Comprehend the type of warhead that should be selected against specific targets such as armour, maritime vessels, aircraft, structures and humans.

## Slide 3
Introduction to Warheads
A warhead designer must devise a warhead capable of inflicting the required damage within the constraints imposed by the delivery system
Most warheads are delivered to the target by a missile system, which possesses KE.
Reliance solely on KE has two disadvantages:
  the system may have inadequate KE at achievable velocity to cause adequate damage to the target given a hit, or the KE has not been fully coupled; and
  The system may not be sufficiently accurate to guarantee a hit with acceptable probability
A warhead is therefore used because:
  It is an efficient way of increasing the amount of destructive energy available to the system at the moment of engagement, and improves energy coupling to the target
  It allows the destructive effect to be better matched to the likely response of the target (choice of lethal mechanism)
  It allows the missile to miss the target by a limited distance but still be effective

## Slide 4
Explosive parameters of interest
Kinetic energy and kinetic energy density are hugely important for energy coupling, but so is blast overpressure and impulse – these are equations you will get to know

## Slide 5
Warhead components
Whatever the system may be, the warhead basically consists of the following components:
  The payload
  The fuzing system
  The safety and arming unit, or SAU
The effectiveness of the warhead may be varied by changing any or all three basic components, which may not be physically separate items. For example, the fuze and SAU are often combined in complex weapons.
Notes: The payload directly causes the damage. But it may not be explosively destructive – illumination, propaganda leaflets, CBRN.
The fuze initiates the payload so that it produces the right effect at the right moment. It must detect the target and initiate at the moment of maximum effect. This may be in the ms bracket and is therefore dependent on trajectory, speed and flight. Data may be gathered from self-generated energy (active), or from energy emitted from the target (passive). Impact, proximity, delayed function.
The SAU has two primary functions: prevention of accidental detonation of the warhead, usually by interrupting the explosive pathway between fuze and payload; and providing the detonation pathway between fuze and payload by removing that interruptor device in the fuze. The SAU may also include a self-destruct, self-neutralize (example mines), or delayed arming to protect friendly forces.

## Slide 7
The explosive train
A combination of energetic mixtures:
The initiator (detonator) and booster (intermediary) are often part of the fuze and/or SAU
The detonator may be initiated electrically, or by impact or pyrotechnic delay
The main charge may be designed for high brisance, lift, or heave.

## Slide 8
Factors affecting performance
Energy coupling
Dispersion
Damage volume
Attenuation
Propagation

## Slide 9
Energy coupling and Attenuation
Energy coupling is the transfer of the warhead’s destructive energy at the target.
To take a simple case, a high velocity KE penetrator could pass straight through a light structure and leave it fully functional. However, it could dump much of its KE to overmatch a heavy armour plate and still have residual energy to inflict damage inside the crew compartment.
As blast and fragments radiate from a point of detonation their destructive power is reduced the further they travel. This loss of power is called attenuation. Eventually attenuation will result in a limiting velocity whereby damage is not possible.

## Slide 10
Dispersion
If a series of identical missiles are fired at a target, and the miss-distance plotted, the resulting distribution is known as dispersion.

## Slide 11
Damage volume
The effectiveness of any warhead decreases with increasing distance from target. There is a 3-D boundary relative to the surface of the warhead within which the effect is lethal and which is called damage volume
A KE projectile without a warhead has a damage volume equal to the diameter of the projectile

## Slide 12
Propagation
The manner in which energy and material from the detonating warhead travels through the medium in which the blast occurs is known as propagation
If uniform propagation occurs in all directions then this is known as isotropic propagation, otherwise as non-isotropic propagation
Anisotropy may occur when a warhead has been specifically designed to produce a certain fragmentation effect.

## Slide 13
Anisotropy

## Slide 14
Types of Warhead Lethal Mechanism

## Slide 15
The simplest and cheapest warhead
It relies on the shock wave effects produced when the explosive detonates
  External blast: designed to detonate near the target and cause damage provided the target is within the damage volume of the warhead
  Internal blast: designed to penetrate before detonation, and must heat the target and overmatch the material properties by penetration or perforation
Blast

## Slide 16
Fragmentation
Naturally fragmenting warhead – seldom used in GW warheads but used extensively in artillery and infantry / common user
Controlled fragmenting warheads – fragment shape and size controlled. Sub-groups are discrete fragments (discrete/continuous rod) and ‘fire-formed’ fragmentation systems used to encourage case break-up

## Slide 17
These warheads focus the explosive energy in a given direction to achieve penetration of the target. They are mainly concerned with the attack of well protected targets such as armour. These groups include:
  Shaped charges
  Explosively formed projectiles (EFPs)
  High explosive squash heads (HESH)
Directed Explosive Energy

## Slide 18
Kinetic energy
Biological
Chemical
Radiological
Nuclear
Other types of warhead

## Slide 19: But what about thermal effects?
Critical Energy Levels for a Human | 
Energy absorbed (after 55 oC) per unit surface (kJ m-2) | EFFECT
>41.8 | Pain, mild second-degree burn
>83.6 | Blister, severe second-degree burn
>167 | Severe third-degree burns, permanent injury

## Slide 20: But what about thermal effects?

## Slide 21: Equations for thermal output
where NEQ is mass of explosive in kg, and R = the distance at which 167 kJ m-2 is produced
where d = diameter of fireball (m) and Q = the mass of explosive burning (kg)
where t (s) = duration of fireball

## Slide 22: Heat of Afterburn
The detonation products are fuels i.e. C, CO, can add energy similar to excess Al, Mg, Zn etc.
When they expand in the air, and if they are at high enough temperature, they will burst into flames.
The ‘afterburn’ or secondary fireball can be very energetic
The heat evolved is the difference between the heat of combustion of the original explosive and its heat of explosion

## Slide 23: Example (TNT Afterburn – the easy way)
Consider TNT -
The CO and C are the fuels and will burn in air to produce:
Therefore, kJ/mol
Heat of explosion TNT = -929.34 kJ/mol, therefore the heat of afterburn is 2.5 x higher!!!!

## Slide 24: Example (TNT Afterburn – slightly harder)
Consider TNT -
Therefore, kJ/mol
Therefore, kJ/mol

## Slide 25
Warhead design and selection
Warhead design starts with a target assessment, which should identify the make-up of the target, its strengths and it weaknesses (SWOT analysis!):

## Slide 26
Warhead design and selection

## Slide 27
Warhead design and selection (assessment of effect)
Knowing the target, it is possible to determine the best lethal effect required, or the damage level required
Knowing the munition, it is possible to determine the conditions under which it will provide the required level of damage
The effectiveness of the munition depends upon:
Required level of damage
Distance
Intervening medium (such air, water, armour, composite structures)
The relative velocities of the target and warhead

## Slide 28: Warhead design and selection
Lethal Mechanism
Type of Target
Type of Ammunition
The Explosive Train and Safety & Arming
Blast
  Overpressure and impulse
Fragmentation
  Natural or Pre-Formed?
  Kinetic Energy Density for Perforation
Directed Energy
  Shaped Charge
  EFP
  HESH
Non-lethal applications (crowd control / denial)
What lethal mechanisms does the designer have at their disposal?

## Slide 29: Warhead design and selection
Lethal Mechanism
Type of Target
Type of Ammunition
The Explosive Train and Safety & Arming
Human (protected / unprotected)
Ships
Submarines
Aircraft
Helicopters
Structures
Equipment
The types of target that may be considered in any given engagement scenario

## Slide 30: Warhead design and selection
Lethal Mechanism
Type of Target
Type of Ammunition
The Explosive Train and Safety & Arming
Tube Fired
Guided Missile
Rocket System
Air Dropped
Emplaced
Potential considerations of the delivery system for a type of ammunition

## Slide 31: Warhead design and selection
Guns
  Field
  Tank
  Rifle / Smooth bore
Mortar
  Smoothbore
  Rifled
  Muzzle / Breach loading
Tube Fired
Guided Missile
Rocket System
Air Dropped
Emplaced
Potential considerations when designing a tub-launched system

## Slide 32: Warhead design and selection
Anti-Ship
Anti-Air
Anti-Ground
Effect
  Blast / fragmentation
  Directed energy
    Shaped Charge
    EFP
  KE (HVM)
Tube Fired
Guided Missile
Rocket System
Air Dropped
Emplaced
Potential considerations when designing a guided missile

## Slide 33: Warhead design and selection (armour)
Perforation
  Heavily armoured at front (thick, sloping armour, composite?)
    Limited choice of perforation mechanisms
  Less well armoured top, sides and bottom
    Greater choice of perforation mechanism
Blast
  Very resistant if closed down
  Large blast beneath vehicle is effective
Schematic of lethal mechanism choice against an armoured vehicle

## Slide 34: Warhead design and selection (structures)
Hard Targets
  Structure
    Monolithic
    Layered
    Combination
  Where to detonate
    Robust munition, including fuze
  Collateral damage (proportionality)
Successful destruction of ammunition facilities in Libya using anti-structures munitions - Paveway

## Slide 35: Warhead design and selection (maritime)
Surface ships (huge range of sizes)
  Frigate 2800 tonnes
  Aircraft Carriers 60,000 tonnes
  High buoyancy, multiple bulkheads (10 – 30 mm thick, 100 m3)
Submarines
  Small volume within hull
  Little reserve buoyancy
  Outer hull provides good protection
Type 45 and Astute Class Submarines

## Slide 36: Warhead design and selection criteria (aircraft)
Altitude hugely affects what warhead can be used
Internal/external blast, pros and cons
Kinetic energy, pros and cons
Fragmentation
Discrete or continuous rod at high altitude

## Slide 37
Warhead design and selection – a summary
Key:
SC = shaped charge
IB = internal blast
EB = external blast
CR = continuous rod
BL = bomblet
FR = fragmenting

## Slide 38
Sources of energy example
What is the total energy that can be delivered to an aircraft from a surface-to-air missile given the following data: mass of missile 250 kg, velocity 920 ms-1, warhead mass 10 kg, energy of detonation per kg is 4MJ:
KE available = 0.5 x 250 x 9202 = 105 MJ
Explosive energy (chemical energy) available = 10 x 4 = 40 MJ
Therefore, total energy imparted to target = 145 MJ

## Slide 39
Sources of energy example (the Twin Towers)
What was the total energy that could be delivered to the North Tower from a Boeing 767 aircraft: mass of fully laden aircraft 142,000 kg, velocity 265 ms-1, fuel mass 72,000 kg, energy of detonation per kg is 43MJ:
KE available = 0.5 x 142000 x 2652 = 5000 MJ (4,985,975,000 J)
Explosive energy (chemical energy) available = 72000 x 43 = 3000 MJ
Therefore, total energy imparted to target = 5000 MJ + 3000 MJ = 8000 MJ = 2000 kg TNT

## Slide 40: Overpressure experienced between 93rd through 99th Floors of North Tower
69 kPa is almost complete destruction of a reinforced building, but what about reflected pressures?

## Slide 41: Summary
Explosives engineering is all about selecting an explosive to perform a function against a target, or to produce an effect in the visible or non-visible spectrum
The family of explosives is very small (low explosives and high explosives), but their utility is vast:
  this could be blast, fragmentation, directed energy, a combination of all three;
  the production of light, sound, and heat; or
  to accelerate munitions to the target, whether this be indirect or direct fire
We must match the warhead to the target, considering all the criteria associated with LOAC (more later)
We must consider the whole system, not just sub-systems or components in design
The choice of explosive is hugely dependent upon whether we want to achieve blast or fragmentation, hence you will learn the terms detonation pressure, overpressure, impulse duration, brisance, ideal / non-ideal explosive, fuel air explosive, enhanced blast, thermobaric and many more.
It is all about oxygen balance and the energy of formation of the detonation/combustion products