## Slide 1: How do Industrial Operations Measure & Manage Their Efficiency & Energy Consumption? Joseph Blackmore (1702858) Andrew Thorn School of Engineering BEng (Hons) Energy & Environmental Engineering
School of Engineering
Introduction
This project is a collaboration between myself and a thermoplastics manufacturing facility based in the village of Kenfig, Bridgend. The motivation behind carrying out this project was the ability to apply the knowledge gained in my energy related modules throughout my degree to a real-world situation. The ability to have discussions with a plant manager at a working facility offered valuable experience and insights into the practical challenges of planning and implementing efficiency related engineering and management solutions.
Project Aims
To experience how a working factory goes about measuring their energy usage and how potential areas for improvement are evaluated.
To explore the incentives for a business to strive for improved efficiency and reduced energy consumption.
Carry out research into energy auditing techniques and how they are used to highlight areas for improvement in energy usage.
To understand the importance of working towards improved efficiency on a global scale.
To evaluate the feasibility of real-world engineering solutions to improving efficiency in a manufacturing facility.
To research why there is an increase in pressure on industry to reduce emissions.
Methodology
By applying the principles of a diagnostic energy audit to a working industrial facility, a comprehensive understanding of how an industrial operation physically measures and applies management techniques in order to reduce its energy consumption can be established. By collecting primary data and using data analysis to determine potential areas for improvement, the analytical, mathematical and practical skills that an engineer must possess will need to be implemented.
Results
Firstly, analysis into the perceived performance of the facilities Energy Management System (“EnMS”) was carried out. Employees with varying roles completed a detailed questionnaire designed by The Carbon Trust.
Graph 1: Highlighting areas for improvement in the Energy Management System
Chart: Comparison Between Communication Rating and Overall Rating
| Distribution Manager | Quality Inspector | Quality Manager | Plant Manager | Continuous Improvements Engineer | Engineering Technician | Packer
Communication Rating (%) | 80 | 90 | 30 | 50 | 30 | 20 | 10
Grand Total Rating (%) | 73 | 68 | 67 | 75 | 64 | 60 | 21
The results of this questionnaire suggested that whilst most of the employees at the facility perceived the “EnMS” to be of acceptable quality, Communication was perceived to be an area of weakness that requires immediate attention by multiple employees. Estimations for the financial savings and reductions in carbon footprint possible by implementing engineering solutions to achieve the energy conservation opportunities identified by the energy audit were then completed;
 | Production ‘A’ | Production ‘B’ | Warehouse & Racking Area
No. units for modification | 36 | 30 | 33
Existing System | 400W Low Bay (Metal Halide) | 400W Low Bay (Metal Halide) | 400W Low Bay (Metal Halide)
Proposed New Lighting Scheme | 4 by 49W T5 Low Bay (LED) | 4 by 49W T5 Low Bay (LED) | 4 by 49W T5 Low Bay (LED)
No. Tubes per fitting (existing) | 1 | 1 | 1
No. Tubes per fitting (new) | 4 | 4 | 4
Control to be added | No | No | Yes
Daily Load hours with added control (hrs/day) | 24 | 24 | 6
Current Daily Load Hours (hrs/day) | 24 | 24 | 24
Days per working year | 363 | 363 | 363
Current annual operating hours (hrs/year | 8712 | 8712 | 8712
Annual operating hours with added control (hrs/year) | 8712 | 8712 | 2178
Electricity price (£/kWh) | 0.088 | 0.088 | 0.088
Power of existing system | 400W | 400W | 400W
Power of new system | 196W | 196W | 196W
Running cost of existing system (£/year) | 36x0.4kW= 14.4kW 14.4kWx8712 hours= 125,452.8 kWh, x £0.088 = £11,039.85 | 30x0.4kW= 12kW 12kWx8712 hours= 104,544 kWh, x £0.088 = £9,199.87 | 33x0.4kW= 13.2kW 13.2kWx8712 hours= 114,998.4 kWh, x £0.088 = £10,119.86
Running cost of new system (£/year) | 36x0.196kW= 7.056kW 7.056kWx8712 hours= 61,471.87 kWh, x £0.088 = £5409.52 | 30x0.196kW= 5.88kW 5.88kWx8712 hours= 51,226.56 kWh, x £0.088 = £4507.94 | 33x0.196kW= 6.468kW 6.468kWx2178 hours= 14,087.304, x £0.088 = £1239.68
Annual savings (£/year) | £5630.33 | £4691.93 | £8880.18
Total investment | £9462 | £9462 | £9462
Payback time to the nearest Month | 20 | 24 | 13
Annual reduction in carbon footprint (kg CO2) | 0.25358 x 63,980.93 = 16224 kg | 0.25358 x 53,317.44 = 13520 kg | 0.25358 x 100,911.096= 25589 kg
Table 1: Results of LED replacement payback calculations
Chart: Energy Consumption Taken Every 15 Minutes Over 24 Hours
Graph 2: Analysing Scrap Grinder energy usage patterns
Scrap grinders were left idling for significant periods of time, by automatically switching off grinders an annual saving of £14,534 could be achieved.
Conclusions
Industrial operations carefully measure their energy usage through analysis of energy invoices and through data logging systems such as through an interconnected PAC set-up. By analysing the energy usage of specific machines and systems, targeted plans to improve efficiency in specific areas can be produced. Management of energy usage and efficiency is often achieved through implementing an ISO50001 accredited energy management system.