## Slide 1: Track test Exercise Week 3

## Slide 2: Task 2
Development of a spreadsheet to determine wheel loads when cornering

## Slide 3: Spreadsheet Layout
ay | Lateral Acceleration [m/s/s] | 9.81 |  |  |  |  |  |  |  | 
Measured Suspension Data |  |  |  | Calculated Suspension Data |  |  |  | Results |  | 
MR lf | From WinGeo3 | 1 |  | Ms lf | Left front corner sprung mass [kg] | 225.0 |  | Kϕf | Front Roll Stiffness [Nm/rad] | 112500.0
MR rf | From WinGeo3 | 1 |  | Ms rf | Front Right corner sprung mass [kg] | 225.0 |  | Kϕr | Rear Roll Stiffness [Nm/rad] | 112500.0
MR lr | From WinGeo3 | 1 |  | Ms lr | Rear Left corner sprung mass [kg] | 225.0 |  | Kϕt | Total Roll Stiffness [Nm/rad] | 225000.0
MR rr | From WinGeo3 | 1 |  | Ms rr | Rear Right corner sprung mass [kg] | 225.0 |  | Mot | Overturning moment [Nm] | 1765.8
M lf | Left front total measured static corner mass [kg] | 250 |  | Ms f | Total front sprung mass [kg] | 450.0 |  | ϴ | Roll angle | 0.0078
M rf | Right rear measured static corner mass [kg] | 250 |  | Ms r | Total rear sprung mass [kg] | 450.0 |  | WTsf | Front weight transfer due to spung mass [N] | 588.6
M lr | Left rear total measured static corner mass [kg] | 250 |  | Musf | Total front unsprung mass | 50 |  | WTsr | Rear weight transfer due to spung mass [N] | 588.6
M rr | Right rear total measured static corner mass [kg] | 250 |  | Musr | Total rear sprung mass [kg] | 50 |  |  |  | 
Mus lf | Left front unsprung mass [kg] | 25 |  | Kslf | Front Spring rate [N/mm] | 100.0 |  | WTsrcf | Sprung mass at RC Height | 294.3
Mus rf | Right front total unsprung mass [kg] | 25 |  | Ksrf | Right front spring rate [N/mm] | 100.0 |  | WTsrcr | Sprung mass at RC Height | 294.3
Mus lr | Left rear unsprung mass [kg] | 25 |  | Kslr | Left rear Spring rate [N/mm] | 100.0 |  | Wtusf | Unsprung mass at wheel centre height | 98.1
Mus rr | Right rear unsprung mass [kg] | 25 |  | Ksrr | Right Rear Spring Rate [N/mm] | 100.0 |  | Wtusr | Unsprung mass at wheel centre height | 98.1
Ksf | Front Spring rate [lb/in] | 583.1 |  | Kw lf | Left front wheel rate [N/mm] | 100.0 |  |  |  | 
Ksf | Front Spring rate [lb/in] | 583.1 |  | Kw rf | Right front wheel rate [N/mm] | 100.0 |  | Fz lf | Left front vertical force [N] | 3433.5
Ksr | Rear Spring rate [lb/in] | 583.1 |  | Keslr | Effective rear spring rate [N/mm] | 100.0 |  | Fz rf | Front Rightvertical force [N] | 1471.5
Ksr | Rear Spring rate [lb/in] | 583.1 |  | Kesrr | Effective rear spring rate [N/mm] | 100.0 |  | Fz lr | Rear Left vertical force [N] | 3433.5
Tf | Front Track | 1.50 |  | b | distance of cg from front axle [m] | 1.000 |  | Fz rr | Rear Right vertical force [N] | 1471.5
Tr | Rear track | 1.50 |  | hr -hf | Rear -Front RC Height [m] | 0.000 |  |  |  | 
L | Wheel base | 2.00 |  | z | Depth of triangle at CG [m] | 0.000 |  | Check | Total sprung car WT | 1962.0
Rr | Rolling Radius | 0.30 |  | z+hf | Height of roll axis at CG [m] | 0.100 |  | Check | Total solid car WT | 1962.0
H' | Height of CG above ground | 0.3 |  | H | Height of CG above roll axis [m] | 0.200 |  | Check | Total vertical load from vertical forces | 9810.0
hf | Height of Front roll centre above ground from Win Geo 3 | 0.100 |  |  |  |  |  | Check | Total vertical load from corner masses | 9810.0
hr | Height of Rear roll centre above ground from Win Geo 3 | 0.100 |  |  |  |  |  |  |  |