## Slide 1: Creating our Solution

## Slide 2
WHAT NEXT ??
… Design !
Can we get on with designing stuff now PLEASE??!!
Notes: This cartoon contains a serious message!
Designers are eager to design things… they generally do not like ‘faffing about’ doing things in teams which seem pedantic and ultra-systematic!
There must be infrastructural pressure in place to ensure that these ‘other’ activities are done thoroughly, at the right time.
Design reviews should do this, with specific deliverables baked into the NPD process gateways.

## Slide 3: Creating Candidate Concept Solution
No Great Thing is Created Suddenly
Epictetus AD 55-135
Notes: Now we will move on to cover the processes for MANAGING RISK.
Part 02 of the Handbook, particularly Section 9.4.
Key activities of recognising what Hazards might apply, exploring and understanding them and then controlling the Risks.

## Slide 4: Where are we? BAE Systems’ Design System Process (RFCD)
Customer
Needs and Expectations
User
Requirements
Subsystem
Requirements
Build and Check Requirements
Design System
System Requirements
System
Design
Definition

## Slide 5: Creating Candidate Solution Concept (C)
Principles
The Principles of the Perform Creating Candidate Solution Concepts process are:
A number of viable candidate solution concepts should be considered.
The chosen solution concept should be identified from the candidates by employing an appropriate analytical approach.
The selected solution concept should be agreed with all interested parties.
Objective
The identification, assessment and selection of solution concepts is an integral part of the Engineering Lifecycle and the Creating Candidate Solution Concepts process should be used:
To ensure the widest practicable range of solution options is created in response to a requirement.
To support the progressive down-select of options to the point where full engineering resources can be confidently invested to detailing the selected solution.
To ensure that the selection process for design options adequately considers the full range of design drivers, both from a Customer and Enterprise viewpoint.
To ensure the Enterprise retains full traceability of selection and de-selection rationale for future reference.
Verification
The performance of this process should be verified with Design Review and quality audits.
Extracted from LM0502-03

## Slide 6: A Systems Approach to Design
Objective
The identification, assessment and selection of solution concepts is an integral part of the Engineering Lifecycle and the Creating Candidate Solution Concepts process should be used:
To ensure the widest practicable range of solution options is created in response to a requirement.
To support the progressive down-select of options to the point where full engineering resources can be confidently invested to detailing the selected solution.
To ensure that the selection process for design options adequately considers the full range of design drivers, both from a Customer and Enterprise viewpoint.
To ensure the Enterprise retains full traceability of selection and de-selection rationale for future reference.

## Slide 7: A Holistic Approach to Arriving at the “best” Solution
System
Requirements
Functions
and Performance
Measures
Divergent Thinking
Convergent Thinking
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Concept
Concept
Concept
Concept
Concept
Solution
Concept(s)
CONCEPT GENERATION
Use functionality as a means of handling complexity yet simultaneously ensuring whole system coverage to generate all possible functional solutions
CONCEPT INTEGRATION
From the set of all possible solutions determine those combinations that form a whole system concept
CONCEPT
SELECTION
Evaluate the whole system concepts to identify the “best”

## Slide 8: Functions the heart of the Systems Approach
I Want
FUNCTIONALITY
Translate Stakeholder Requirements into
Translate Functionality into
system solution
It Works!

## Slide 9: Concept Generation
System
Requirements
Functions
and Performance
Measures
Divergent Thinking
Convergent Thinking
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Idea
Solution
Concept(s)
CONCEPT GENERATION
Use functionality as a means of handling complexity yet simultaneously ensuring whole system coverage to generate all possible functional solutions
CONCEPT INTEGRATION
From the set of all possible solutions determine those combinations that form a whole system concept
CONCEPT
SELECTION
Evaluate the whole system concepts to identify the “best”

## Slide 10: Function Means Analysis
What is it?
  a tool for generating, capturing, selecting and documenting system design concepts.
Why do it?
  Function Means analysis uses the uncovered generic and other functionality to ensure the holistic generation of candidate system concepts
How to do it
  Function Means Analysis has two stages:
    Stage 1:Concept Generation: a divergent thinking activity where the functions of the system are considered in turn and the means of achieving those functions identified
    Stage 2:Concept Integration and Selection: a convergent thinking activity that identifies whole system concepts
Mower Solution. Link to Spreadsheet

## Slide 11: Function Means Analysis Process
Stage 1
Stage 2

## Slide 12: Step 1: Identify Functionality
To undertake a Function Means Analysis requires knowledge of the functionality of the system. The functionality should be:
  Complete i.e. encompass the whole of the system
  At the same level of generality
These rules are not rigid. Indeed, Function Means Analysis can help to check whether the system functionality is complete. Very few systems are unprecedented and therefore a check can be made to ensure that the current system solution sits within the means identified – if not then perhaps we are missing some functionality
Once identified the functions should be entered in the Function column of the Function Means Table

## Slide 13: Step 2: For each Function Generate Solutions
Taking each function in turn, the team should identify and record in the table ALL the POSSIBLE means of achieving that function
Quantity rather than quality is the aim at this point and a good rule of thumb is to aim for 9 ideas per function. This assumes 3 conventional, 3 extreme and 3 with high potential. Ridiculous, silly, impractical ideas should not be shot-down, ridiculed, or ignored – write them down
If it is difficult to generate solutions to functions:
    The function my be a pseudo-function like “generate style” these either need rewriting as “proper” functions or removing
    The function description may be at too high a level and needs to be decomposed into a number of lower level functions for which design options can be explored

## Slide 14: Tracer Example Function Means Analysis
Tracer Functionality from QFD
Solutions (means) to Functionality

## Slide 15: Exercise: FMA Stage 1
In small teams
Construct a Function Means Chart for the case study problem - consider all solutions
Time: 30 minutes

## Slide 16: Introduction to Concept Integration and Selection
The first stage of Function Means Analysis provides a large number of potential functional solutions. The task now is to:
  Generate a number of complete candidate solution concepts frequently referred to as design or concept system solutions – this is called Concept Integration

## Slide 17: Concept Integration
The purpose of Concept Integration is to arrive at a number of potential whole system solution concepts
  We often use the word integration to mean just the final “physical” integration of a system – but the decisions we are about to make are fundamentally integration decisions and poor choices at this point in time, will have detrimental effects on the physical integration of the system
Assuming that the concept generation has been done by Function Means Analysis, there are a number of strategies for Concept Integration
  Identify the “best” means for each function
    cannot guarantee an optimal system solution
  Consider every permutation from the function means analysis
    will take too long
  Reduce the number of options and develop a limited number of potential whole concept solutions
This last strategy can be accomplished using the Function Means Chart

## Slide 18: Function Means Analysis Process
Stage 1
Stage 2

## Slide 19: Step 3: Determine Selection/De-selection Criteria
What is required at this step are some key criteria that can be used to quickly eliminate or promote the solutions documented in the Function Means Table
The aim is to remove the obvious “sore-thumbs”
A good starting point for the criteria is the primary WHATs from the QFD 1. These are customer facing and therefore deselecting functional solutions that do not meet these will ensure that only “compliant” ideas are carried forward
The general recommendation here is between 3 and 6 criteria. Too many criteria can make the process time consuming. The drawback, of course, with few criteria is that those that are selected have a significant impact on the selected system solution – the wrong criteria leads to the wrong solution
A simple example: consider a domestic toaster. The User Requirements might be:
User Requirements for a Domestic Toaster
Even toasting
Quick
Affordable
Easy to use
Attractive
Reliable
Easy to clean
Energy Efficient
4 slices at once
Etc.
Key requirements that can be used to deselect functional solutions those that are easy to apply like:
Even Toasting
Affordable
Easy to clean
Energy Efficient
Requirements like “Attractive” and “Reliable” are less easy to apply – at this stage.

## Slide 20: Step 4: Use the criteria to de-select from the Table
The criteria, determined in the previous step, are now systematically applied to the removal of candidate functional solutions
The aim here is to remove approximately 50% quickly, i.e. the obvious “sore thumbs”
As functional solutions are removed a note should be made of the criteria and reasoning that led to their removal
Over arguing at this point is counter productive – functional solutions that generate “excessive” debate should be retained

## Slide 21: Toaster Example
Key:
✘ Even Toasting
✕ Affordable
✶ Easy to clean
❋ Energy Efficient
✘
✘
✘
✘
✘
✘
✘
✘
✘
✘
✘
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✶
❋
✕
✕

## Slide 22: Step 5: Review Remaining Options to Generate Potential Whole System Concept Solutions
With the “trees removed” the task now is to determine potential whole system concepts
A simple approach here is to plot routes through the table that represent complete system concepts
For any given function as many means as necessary can be selected for a particular whole system concept – note though if several solutions are necessary it could be a consequence of the function being at too abstract! In such situations it is worth considering decomposing the high-level function into lower-level functions
Selecting the “routes” can be based on technologies that are compatible or avoid incompatibilities
The aim should be to generate as many whole system concepts as realistically possible – common sense should also prevail

## Slide 23: Toaster Example
Key:
✘ Even Toasting
✕ Affordable
✶ Easy to clean
❋ Energy Efficient
✘
✘
✘
✘
✘
✘
✘
✘
✘
✘
✘
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✕
✶
❋
✕
✕

## Slide 24: Tracer Example Function Means Analysis
Tracer Functionality from QFD
Solutions (means) to Functionality

## Slide 25: Exercise: Concept Integration
In small teams
Consider your Munition Function Means Table
Identify 3-6 de-selection criteria and apply them to your Function Means Table to eliminate non-compliant functional solutions
Review the remaining potential functional solutions to create two/three potential whole concept system solutions for the case study Munition
Time: 30 Minutes

## Slide 26: A Model Answer!
De-selection criteria
Link to Spreadsheet

## Slide 27: Summary: FMA
Pros
Simple to use
Allows the design problem to be logically broken down into manageable elements for which solution options can be easily found
When used with an open mind is extremely powerful for identifying and recording “all” possible design options
The Function Means Table allows all the design options to be displayed simultaneously allowing for easier review
Applicable at any level of design
Visual and structured tool for the systematic identification of whole concept solutions
Captures in a simple way the justified design rationale
Encourages team discussion and consensus decision making
Cons
Getting the functions at the correct level of abstraction in order to explore solution choices
The outcome can be a significant number of options which must be combined together
Sometimes viewed as too simplistic and therefore not a serious tool
Ensuring the “best” de-selection criteria
High level concepts can incorporate many “means”
Tips
Manage the number of functions to 15 – 20
If a function doesn’t yield many solutions check that it is not too abstract
Don’t exclude solutions during the first phase
Consider using diagrams to explain ideas
Check the table contains any existing system designs
Use the User/Stakeholder requires for the de-selection

## Slide 28
Concept Selection
(and evaluation)

## Slide 29: Concept Selection/Evaluation
The purpose of Concept Integration is to identify many alternate potential complete system solutions
The purpose of Concept Selection/Evaluation is to arrive at the best possible and feasible system solution from the candidate list or at least eliminate the weaker options
A very useful tool is the Pugh Matrix

## Slide 30: The Pugh Matrix
What is it?
The Pugh Matrix is useful when comparing a number of alternatives and for finding which best meets a set of requirements/criteria
Why do it?
To quickly identify the best concept or eliminate the weaker ones
When to use it?
Whenever attempting to decide between a number of alternate system concept designs
Particularly useful when there is relatively large number of key customer requirements/criteria
Who Does it?
Best performed by a team that includes all interested disciplines and functions

## Slide 31: Pugh Matrix Process- How to do it
STEP 1: Determine evaluation – selection criteria
STEP 2: Select “standard” design concept for comparison
STEP 3: Compare options against “standard” and determine total score
STEP 4: Undertake qualitative optimization through consideration of hybrid concepts
STEP 6: Evaluate results for a decision
STEP 5: Evaluate criteria weighting and sensitivity analysis

## Slide 32: How to Do it: Steps 1 to 3
Step 1:
Determine suitable evaluation criteria. The customer facing requirements particularly the key Non-Functional System Requirements are sensible. It is important that these should be supplemented by other stakeholder requirements - criteria that reflect other stakeholder views – particularly those of the business
It is vey important to have a clear definition of each criterion
Step 2:
One design concept is selected to be the “standard”. All criteria are scored ‘S’ for “Standard”. If appropriate, a good choice is to use the previous design for the standard because it exists and therefore its performance should be well known
Step 3:
Compare each design concept against the “standard”, “requirement by requirement” and decide a “pair-wise score with
  S = same
  + = better
  - = worse
Can use ++ for much better and - - for much worse. Record decisions and rationale
Sum the +’s and –’s to determine the Total Score
Always record rationale behind decisions

## Slide 33: How to Do it: Step 4
Step 4:
Having scored each candidate design option, consider hybrids by combining where possible the best from each alternative. This is a form of qualitative optimisation.
Concept BC – a hybrid between Concepts B and C

## Slide 34: How to do it: Steps 5 & 6
Step 5:
The ability of the Pugh Matrix to discriminate between concepts can be improved by weighting the criteria
The weighting is usually a simple 1 to 5 scale with 1 of the lowest importance and 5 of the highest
It is also possible to perform a simple sensitivity analysis to assess the impact of small variations in the weightings – i.e. conclusions should be insensitive to small variations in the weightings
Step 6:
Make the decision and record reasons behind decisions. Quite often there is no clear “winner” but there is often a clear “loser” in such cases perform a sanity check (does the decision make sense) and remove the losing option.
If you do have weightings – don’t use them for the first pass to rank system solutions. Use them on the second pass – if the system solution ranking order is unchanged you have evidence of a robust decision.

## Slide 35: Double Check
The strength and weakness of the Pugh Matrix is the pairwise comparison against a standard. We need to be consistent in our judgments
If we judge option A to be + (better) than the standard and option B to be – (worse). To be consistent Option A must be what compared to B?
A good consistency check is having found a winner that is not the standard, it is good practice to make it the standard, redo the pairwise comparison to test consistency, the ranking should be the same!

## Slide 36: Exercise: Pugh Matrix
In small teams
Use a Pugh Matrix to make a final selection for your mower concept
Time: 30 Minutes

## Slide 37: The Next Step
The next step, having identified a number of candidate whole system concept solutions, is to “work up” the concepts to allow them to be evaluated
This involves:
  Sketching out the physical layout or architecture
  Producing concept drawings – to show what a concept looks like
  Defining the concept of operation – the Use Case or Use Cases for the concept
  Performing “back of the envelope” calculations to determine performance aspects of each concept
  Identifying the solution dependent and architectural functionality necessary as a consequence of the functional solution choices
This last point is very important as it will necessarily introduce design iteration

## Slide 38
End of Level 4

## Slide 39: A Model Answer
Link to Spreadsheet

## Slide 40: Summary: Pugh Matrix
Pros
Provides a rapid assessment of alternative whole concepts
Can use stakeholder requirements to give greater confidence of compliance
Can help develop hybrid system concepts (qualitative optimisation)
Cons
Temptation to use too many requirements slowing down the process
Objective subjectivity! Can select criteria, weightings and scores to obtain any result!
Often no clear winner (but eliminates the weaker options)
Can be treated as a “handle turning” process without thinking

## Slide 41: A Concept Design
Function Means Analysis is a very powerful tool for identifying and capturing potential functional solutions. It also allows the creation of potential candidate system design concepts. However, to down-select, from those candidates it is necessary to add detail by generating concept designs like that shown below:
Such diagrams should be prepared for each candidate system design concept
Link to Spreadsheet

## Slide 42: Munition Architecture and Subsystems
The nature of the selected munition design mean it has 4 distinct subsystems
Case & Charge
Fin Assembly
Shell
Fuze
Note: Not all systems are like this where the architecture and subsystems are obvious. However, irrespective of how the architecture is determined, what is important are the interfaces between the various subsystems.

## Slide 43: There is more to a system than its Generic Functionality
The generic system functionality is not the complete set of system functionality – a system can have functionality that is not generic:

## Slide 44: Top-down & Bottom-up
TOP DOWN
BOTTOM
UP
System
Component
Sub-System
System Use Case Analysis
Functional Analysis

## Slide 45: Schematic For the mower
Transmission
Battery
CPU
Motor
Mulch Collector

## Slide 46: Components for analysis

## Slide 47: Motor blade and height adjust assembly

## Slide 48: Remember there is more to a system than its Generic Functionality
The generic system functionality is not the complete set of system functionality – a system can have functionality that is not generic:
Solution Dependent Functionality: A particular generic function solution may require further solution specific functionality.
Legislation Dependent Functionality: legislation requires us to incorporate additional functionality.
Architectural Functionality: At the system level the collected functional solutions require further functionality typically to support, align, contain and protect.
Emergent Functionality: Functionality aimed at managing Unwanted Behaviour. Usually relates to informing the user of failure situations
So far we have identified solutions to just the generic functionality (and perhaps through FFMEA emergent functions/solutions) to create a number of concept designs
Our choice of solutions will lead to the need to include further solutions to support our choices. If I choose an electric motor as a motivator, I will have to provide an electric power source – a battery for example. These supporting solutions have functionality – solution dependent functionality
The need for architectural elements will also become apparent. These elements have functionality – architectural functionality

## Slide 49: Motor blade and height adjust assembly

## Slide 50: Motor blade and height adjust assembly

## Slide 52
Goup Exercise:-
Identify potential additional functionality in your concept
Solution Dependent Functionality
Legislation Dependent Functionality
Architectural Functionality
Emergent Functionality
Time 30 minutes

## Slide 53: We Iterate the Design
Whenever we identify additional solutions (either supporting or architectural), they can be treated as Non-functional Implementation Requirements and used to identify further functions (Functional Requirements) for which alternative solutions can be explored (new rows to add to the Function Means Table)
We should also update all our earlier work (Use Case, Functional Model, QFD 1 etc.)
Functions
Solutions
Functions
Increasing maturity
of knowledge about the Stakeholders’ requirements, System Requirements
and system/product information
Solutions
Solutions
Functions
Functions

## Slide 54: Example
The Concept Design
Requires additional solution dependent and architectural functionality – for example:
REGULATE MOTIVE FORCE
SEAL SYSTEM (PRESSURE)
REMOVE HEAT (FROM SYSTEM)
ALIGN INITIATING SYSTEM
SUPPORT FINS
Solution Dependent
Architectural

## Slide 55: Generic Functionality QFD 1
Generic Functions

## Slide 56: Generic Functionality QFD 1 (Mower)
Generic Functions

## Slide 57: Generic + Solution Dependent and Architectural Functionality QFD 1
Generic Functions + Solution Dependent + Architectural Functions

## Slide 58: Generic + Solution Dependent and Architectural Functionality QFD 1
Generic Functions + Solution Dependent + Architectural Functions

## Slide 59: Update Functional Importance
Solution Dependent functionality can also be important especially if it contributes to important generic functionality
It is important, however, to review the calculated importance's to understand why certain functions are important and what impact they will have on the User/Stakeholder.
Design Book Functional Importances for the Case Study Generic Functionality
Design Book Functional Importances for the Case Study Generic+ Solution dependent and Architectural Functionality

## Slide 60: Update Functional Importance
Solution Dependent functionality can also be important especially if it contributes to important generic functionality
It is important, however, to review the calculated importance's to understand why certain functions are important and what impact they will have on the User/Stakeholder.
Design Book Functional Importances for the Case Study Generic Functionality
Design Book Functional Importances for the Case Study Generic+ Solution dependent and Architectural Functionality
Chart: QFD 1 Functional Importances
| Fuel System | Programme system | Signal System | Complete Mission | Detect Stationary Object | Detect Moving Object | Adjust cut height | Know position | Manoeuvre | Cut Vegetation | Stop Cut | Return to Base | Deal with Mulches
 | 225 | 465 | 270 | 555 | 410 | 420 | 165 | 375 | 600 | 315 | 225 | 240 | 120 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 61: Functional Importances :- Comparison
Link to Spreadsheet

## Slide 62: What Now
We have just selected our basic system concept(s)
We are about to do some detailed engineering and analysis to “work-up” the design in more detail so we can specify the sub-systems
This will involve determine sizes, selecting materials, performing stress analysis, etc.
Before we do we should just check the selected concept design will meet its requirements – we need to verify the design concept.

## Slide 63: A key tool for Verifying the design concept is:
Design Requirements.
Customer Requirements
Design Requirement Targets
Solution Requirements
Design Requirements.
Solution Requirement Targets
Realisation Requirements
Solution Requirements
Realisation Requirement Targets
Assurance Requirements
Realisation Requirements
Assurance Requirement Targets
QFD 1
QFD 2
QFD 3
QFD 4





## Slide 64: Quality Function Deployment Phase 2
What is it?
QFD 2 is concerned with capturing the translation of System Design Requirements into Solution Requirements
It can be used to:
  Verify the selected whole concept solution is compliant with the System Design Requirements
  Help define lower-level sub-system requirements
  Help identify Critical Design Parameters

## Slide 65: QFD 2 Process
Step 1: Identify the chart WHAT list requirements
Step 2: Translate WHAT requirements into measurable HOW requirements
Step 4: Determine HOW MUCH for HOW requirements
Step 3: Determine relationships between WHAT and HOW requirements
QFD 2: Transfer System Design Requirements
QFD 2: Translate Design Requirements into Design Solutions
QFD 2: Determine relationships between Design and Solution requirements
QFD 2: Determine Sub-System Requirements
QFD 2 uses the same basic process as for QFD 1
The process steps relate to completing one of the “rooms”
It can take several weeks to complete a room!

## Slide 66: Step 1: Transfer Technical Requirements
The HOWs and HOW MUCHs of QFD 1 are the basis for the WHATs for QFD 2.
QFD 1
QFD 2
System Design
Requirements
The “list” of functions should be complete as possible, including those found during design iterations i.e. including solution dependent, architectural functions

## Slide 67: Step 2: Translate into Solution Requirements
The WHATs of QFD 2 are the HOWS of QFD 1 which now require further definition in terms of the system solution
This is achieved by reference to the concept system solution, adding further decisions as necessary – architectural and supporting solutions
If we have performed a Function Means Analysis, then the translation can be taken directly from the FMA table as a route through the table
The selected concept system solution is written in the HOWs room.
If there are several candidate system solutions then either
  Several QFD 2 can be generated – one for each whole system concept
  A single QFD 2 created with multiple whole system concepts
WHAT
HOW
Solutions
Function
Solution
Solution
Solution
Solution
Technical
Design
Requirements
Design Solution
Solution
QFD 1 HOWs
Function
Function
Notes: This slide shows the second stage of QFD 1 translating the customer requirements into technical requirements that are measurable. In other words HOW we intend to satisfy WHAT the customer requires.
The process is to consider each customer “what” in turn and translate this into technical requirements. These technical requirements should not specify solutions but remain general. Typically this is done by consideration of the functionality or features.
A key point to note here that some of the technical translations may well come from the customer requirement. This is very typical in defence products because the customer has set ideas about what they require.

## Slide 68: Step 3: Determine HOW-WHAT Relationship Matrix
WHAT
Technical
Design
Requirements
HOW
Design Solutions
STRONG relationship
MEDIUM relationship
WEAK relationship
Blank or Sparse row
Function
Blank or Sparse column
Solution
This method allows complex
relationships between the system functionality and system solutions to be depicted and easily interpreted
It also permits cross-checking.
Blank or sparse rows or columns indicate places where the translation of WHATs into HOWS is inadequate
If the QFD 2 is derived from the Function Means Analysis, then the leading diagonal will contain strong relationships. What is of interest is the off diagonal terms! They indicate potential emergent properties, interactions or interfacing issues.

## Slide 69: Tracer Example
QFD 2
Tracer Specification
Importance of solutions
Relationships
Will the Solutions
deliver the functional requirements?
Functional Requirements
from QFD 1
Tracer
Solution from Function Means

## Slide 70: Exercise: QFD 2
In small teams
For the case study exercise transfer functions and a system solution from the Function Means Analysis
Complete the relationship matrix and identify any interesting features
Time: 20 Minutes
Note: The intent here is to introduce QFD2. At this point new functions may have been identified – in reality they should be included in the QFD 2

## Slide 71: Look for “Structure”
We should examine the resultant relationship matrix for “structure” as this will show how the system functionality is provided by the solutions and vice versa. It can help in the management of key design aspects

## Slide 72: Step 4: Flow Down Targets and Ceilings HOW MUCH is Enough?
The fourth element of the QFD 2 chart is flowing down the WHAT-HOW MUCHs to give a set of target values for the chosen the design solution
These are design characteristics/ parameters and targets for for the solutions and specify how good they have to be in order to satisfy the customer
If we are dealing with a system then the HOW MUCHs are sub-system specifications
If we are dealing with components or parts then the HOW MUCHs are the part specifications
At higher system levels the HOW MUCHs may be a simple flow-down, but at the lower levels it will be necessary to undertake detailed design work to obtain the desired information to complete the HOW MUCHs
WHAT
HOW
HOW MUCH
WHAT
HOW MUCH

## Slide 73: Flowing Requirements Down
The relationships indicate that a particular design requirement target value needs to be appropriately “flowed-down” to define the solution requirement target values
What goes in the HOW MUCH boxes depends on the “level” of the system under consideration. If we are dealing with a big system at a high level then each box will contain a Subsystem Requirements
What goes in the HOW MUCH boxes depends on the “level” of the system under consideration. If we are dealing with a big system at a high level then each box will contain Subsystem Requirements

## Slide 74: Tracer Example
QFD 2
Tracer Specification
Importance of solutions
Relationships
Will the Solutions
deliver the functional requirements?
Functional Requirements
from QFD 1
Tracer
Solution from Function Means

## Slide 75: HESH QFD2

## Slide 76: Critical Design Features
The QFD 2 can inform the critical design features

## Slide 77: Mower QFD2

## Slide 78: Mower Critical Design Features
The QFD 2 can inform the critical design features

## Slide 79: Sub-System Requirements
QFD 2 can help us develop Sub-System requirements - in fact the Sub-System requirements SHOULD be ready and waiting

## Slide 80: For the Sub System

## Slide 81: Importances for the Subsystem

## Slide 82: QFD 2 Summary
Pros
Validates that system concept solutions are compliant with the System Design Requirements
Identifies potential system interactions that could result in undesirable emergent behaviour or integration issue
Identifies key/critical design features
Helps in the correct and complete flow-down of requirements to subsystem and ultimately component level
Helps manage requirements and trade-offs
Cons
If several concepts system exist requires the development of several QFD 2
Can take time to complete, particularly the flow-down of HOW MUCH requirements
Tips
Manage the detail – we design in levels, so restrict the QFD to 20x20
Take time to define clearly the functions and the corresponding functional solutions
Complete the relationship matrix is a single half-day session
Delegate the generation of subsystem requirements but review as a team
The actual target values for the design solutions are unlikely to be complete (TBD) until we have undertaken the detailed design