## Slide 1
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk
Module Name : Electronics II
Module Code : ACDA6001
Topic : Finite State Machines
Lecture : 10

## Slide 2: Learning Outcomes
Finite State Machines
At the end of this Lecture, the students can be able to understand
- What is Finite State Machines.
- How to draw the State Diagrams.
- Real-world applications through examples of State Machines.
- Practical demonstration of simulating State Machines.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 3: Finite State Machines
Finite State Machines
A Finite State Machine (FSM) is a computational model used to design and describe the behaviour of systems that can exist in a finite number of states at any given time.
Finite State Machines provide a systematic and formal way to model and analyse the behaviour of systems with discrete states and transitions.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 4
Finite State Machines
Applications
  Digital Logic Design: FSMs are used to design and control digital circuits, including counters and state machines.
  Automated Systems: FSMs are applied in various automated systems, such as elevators, traffic lights, Vending Machines, Aerospace Systems, Security Systems and industrial processes.
  Robotics: FSMs are used to control the behavior of robots, guiding them through different tasks and actions.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 5: Types of FSM (Sequential Circuits)
Finite State Machines
Synchronous Sequential Circuits:
  A digital circuit that performs specific operations on every rising edge / falling edge of a clock signal.
  A Clock is given as input to all the flipflop Simultaneously.
Asynchronous Sequential Circuits:
  An Output that responds to sensor inputs, and transitions between states based on the occurrence of events, without being synchronized to a clock.
  A clock will be provided only to the first Flipflop.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 6: Finite State Machines
Finite State Machines
Example of State Diagram
Example 1: Sensors that detect the presence or absence of an object can be modelled with a two-state state machine.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 7
Finite State Machines
State Diagram: States of Sensors
UWTSD Lectures / ACDA6001 – Electronics 2
a
b
1/1
0/0
0/0
1/1
Inputs or Events/Outputs or Actions
State or Present State
1/1
Transitions or Next States

## Slide 8: State Diagram
Finite State Machines
States: Distinct conditions or modes that a system can be in.
Transitions: Rules or conditions that determine when and how the system moves from one state to another.
Events or Inputs: Triggers that cause the system to transition between states.
Actions or Outputs: Responses or behaviours associated with transitions.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 9
Finite State Machines
State Table:
UWTSD Lectures / ACDA6001 – Electronics 2
Input x | Present State (Qn) | Next State (Qn+1) | Output Z
0 | a | a | 0
1 | a | b | 1
0 | b | a | 0
1 | b | b | 1
a  Inactive State
b Active State
Input : 0No Motion of Object 1Motion of Object
Output : 0LED OFF
1LED ON

## Slide 10
Finite State Machines
State Assignment:
Assign : a0 and b 1
UWTSD Lectures / ACDA6001 – Electronics 2
Input x | Present State (Qn) | Next State (Qn+1) | Output Z
0 | 0 | 0 | 0
1 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 11
What is the Characteristic Equation of a D flip-flop
ⓘ Start presenting to display the poll results on this slide.

## Slide 12
Finite State Machines
Excitation Table: Implement the design using D Flipflop
UWTSD Lectures / ACDA6001 – Electronics 2
Input x | Present State (Qn) | Next State (Qn+1) | Output Z | D Flip-Flop D
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 13
Finite State Machines
K- Map: Find the Expression for Output(z) and (D).
UWTSD Lectures / ACDA6001 – Electronics 2
Qn X | 0 | 1
0 | 0 | 0
1 | 1 | 1
Z

## Slide 14
Finite State Machines
Logic Diagram
UWTSD Lectures / ACDA6001 – Electronics 2
Z

## Slide 15
Finite State Machines
Simulation
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 16
Finite State Machines
Example 2 :
Design and implement a Game scoring system using counter that counts in binary but resets to zero after reaching the count of 6.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 17
Finite State Machines
Mod 6 Counter
State Diagram
UWTSD Lectures / ACDA6001 – Electronics 2
f
a
b
c
d
e

## Slide 18
Finite State Machines
State Table
UWTSD Lectures / ACDA6001 – Electronics 2
Present State Qn | Next State Qn+1
a | b
b | c
c | d
d | e
e | f
f | a

## Slide 19
Mod 6 Counter has how many Combinations
ⓘ Start presenting to display the poll results on this slide.

## Slide 20
Finite State Machines
State Assignment
UWTSD Lectures / ACDA6001 – Electronics 2
Present State Qn | Next State Qn+1
q2 q1 q0 | Q2 Q1 Q0
0 0 0 | 0 0 1
0 0 1 | 0 1 0
0 1 0 | 0 1 1
0 1 1 | 1 0 0
1 0 0 | 1 0 1
1 0 1 | 0 0 0
1 1 0 | d d d
1 1 1 | d d d

## Slide 21
Finite State Machines
Excitation Table
UWTSD Lectures / ACDA6001 – Electronics 2
Present State Qn | Next State Qn+1 | Excitation Inputs |  | 
q2 q1 q0 | Q2 Q1 Q0 | J2 K2 | J1 K1 | J0 K0
0 0 0 | 0 0 1 | 0 d | 0 d | 1 d
0 0 1 | 0 1 0 | 0 d | 1 d | d 1
0 1 0 | 0 1 1 | 0 d | d 0 | 1 d
0 1 1 | 1 0 0 | 1 d | d 1 | d 1
1 0 0 | 1 0 1 | d 0 | 0 d | 1 d
1 0 1 | 0 0 0 | d 1 | 0 d | d 1
1 1 0 | d d d | d d | d d | d d
1 1 1 | d d d | d d | d d | d d
Qn | Qn+1 | J | K
0 | 0 | 0 | d
0 | 1 | 1 | d
1 | 0 | d | 1
1 | 1 | d | 0
Excitation Table of JK Flipflop

## Slide 22
Finite State Machines
K- Map Expressions
UWTSD Lectures / ACDA6001 – Electronics 2
Present State Qn | Next State Qn+1 | Excitation Inputs |  | 
q2 q1 q0 | Q2 Q1 Q0 | J2 K2 | J1 K1 | J0 K0
0 0 0 | 0 0 1 | 0 d | 0 d | 1 d
0 0 1 | 0 1 0 | 0 d | 1 d | d 1
0 1 0 | 0 1 1 | 0 d | d 0 | 1 d
0 1 1 | 1 0 0 | 1 d | d 1 | d 1
1 0 0 | 1 0 1 | d 0 | 0 d | 1 d
1 0 1 | 0 0 0 | d 1 | 0 d | d 1
1 1 0 | d d d | d d | d d | d d
1 1 1 | d d d | d d | d d | d d

## Slide 23
Finite State Machines
Logic Diagram
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 24
Finite State Machines
Design a Mod 5 counter using J-K flipflop for an asynchronous Sequential Circuit.
UWTSD Lectures / ACDA6001 – Electronics 2
Step 1:
State Diagram

## Slide 25
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 2:
State Table

## Slide 26
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 3:
State Assignment
a ---> 000
b ---> 001
c ---> 010
d ---> 100
e ---> 101

## Slide 27
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 4:
Excitation Table

## Slide 28
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 5:
K Map

## Slide 29
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 5:
K Map

## Slide 30
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 5:
K Map

## Slide 31
Finite State Machines
UWTSD Lectures / ACDA6001 – Electronics 2
Step 6:
Logic Design

## Slide 32: References
Finite State Machines
[1] "Digital Design" by M. Morris Mano.
[2] "Introduction to Automata Theory, Languages, and Computation" by John E. Hopcroft and Jeffrey D. Ullman.
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 33
Thank you