## Slide 1: Materials Requirement Planning
By
Andrew Thorn

## Slide 2: MRP
Is a computer-based information system used to schedule and order dependent-demand inventories
Two basic inputs were required for the MRP system:
- An order book with the confirmed orders for a
certain time period
- Forecast sales that the organisation believed it
it could sell
The MRP system therefore allowed organisations to make complex calculations of their future needs, and at the same time, achieved this on a large scale

## Slide 3: MRP
Master Production Schedule
Materials requirement Planning
Material Plans
Sales Orders
Forecast Demand
BOM
Available inventory
Bought out parts
Works orders

## Slide 4: MRP Objectives
The MRP system is more than just an inventory system. It is also a scheduling system
There are very few certainties in manufacturing. One certainty is that if things can go wrong, they usually will. This is not the only reason why an operations manager might want to implement an MRP system
The following are also important reasons for implementing an MRP system
- The operating efficiency of the plant needs to be
improved
- The manner in which customers are treated needs
to be improved
- The investment in inventory needs to be minimised

## Slide 5: MRP Objectives
Simply ensuring that enough stock of products is available when customers place orders is not the manner in which customer service can be measured
An organisation should keep its delivery promises. It should also endeavour to cut the lead-time for deliveries
MRP is a powerful tool to assist organisations in keeping to promised deliveries because these promises are locked into the MRP system

## Slide 6: MRP Objectives
The management reports generated by an MRP system enable an operations manager to measure the performance of the manufacturing department
The promises made to the organisation’s customers now become goals of the manufacturing department or division. Once the goals are met on a regular basis, customers will be satisfied
It is important to understand why MRP can and does lower inventory levels. In most manufacturing concerns, a fixed order point system is used when raw materials and components are bought in

## Slide 7: MRP Objectives
Therefore all this stock, plus the safety stock, will remain in inventory until it is used
How can the MRP system help? All material and components requirements are shown in the master production schedule (MPS)
An MPS shows the timing of planned production
The MRP system will space orders so that the material and components arrive shortly before manufacturing requires them

## Slide 8: MRP Objectives
This will dramatically reduce levels of inventory. In response to the reduction in inventory, investment in inventory will also be reduced, which will have a positive impact on the profitability of the organisation

## Slide 9: Dependent Demand Requirements
This type of demand is usually found through forecasts of demand. Dependency of demand means that demand for one item will depend on a demand for another item
An example is the production of a motor vehicle: the demand for tyres and engines is dependent on a motor vehicle being built
A logical consequence of this is that if and when order are received or the organisation projects or forecasts demand for the final product, the assemblies, sub-assemblies and parts needed to manufacture the final product can be determined

## Slide 10: Management of Demand
Once an organisation manages not only orders that are received from customers but also the forecast demand, this can be seen as demand management
One cannot exist without other. Therefore, an organisation must have the correct processes in place to enable it to interface with the market
What are these processes? There is a wide variety of them

## Slide 11: Management of Demand
Examples of these processes include the following:
The keeping of an order book
The entry of sales in the order book
The forecasting of demand
The promising of orders by customers to the sales force
The distribution of the finished product

## Slide 12: Management of Demand
To ensure that the dependent demand is effectively used, it is important that an operations manager has the following knowledge
Information regarding delivery lead times
Bill of materials that are specific
The inventory that is available in stock
An Master Production Schedule
Orders outstanding from suppliers

## Slide 13: Order variation
Happens when customers change their minds about their needs at short notice. For example, imagine that you have ordered a new item of clothing and before taking delivery, you change your mind and inform the store that you no longer require the item of clothing
This is typical of what happens daily in both the manufacturing and service industries
As more and more organisations compete for smaller portions of the market place, flexibility in this regard is seen as the key to having a competitive edge

## Slide 14: Order Variation
If an organisation can not compete on customer satisfaction and flexibility, its chances of survival are seriously hampered
If any supplier is not flexible enough to accommodate the company, the supplier will be removed from the list of suppliers. This example illustrates the complexity of properly managing an order book. If an order book is not managed as it should be, chaos will result

## Slide 15: Basic inputs into the MRP System
MRP System
Three basic inputs
Input 1
MPS
Input 2
BOM
Input 3
Accurate
Inventory
records

## Slide 16: MPS
The MPS is one of the planning inputs of an effective MRP system
For any organisation, the MPS is the most important tool in the planning and control of the manufacturing function
A properly managed MPS will enable an operations manager to ensure customer satisfaction, control inventory levels, and keep manufacturing costs within the budgeted figures
The MPS is the document that spells out what has to be manufactured and by which time the manufactured product should be finished

## Slide 17: MPS
It is therefore very important that the MPS is not overstated or inflated
The capacity constraint that is given by the MPS should also be realistic. A capacity constraint gives the upper and lower limits of a scarce resource’s availability, which is finite and cannot be broken (for example a budget, production plan or capacity plan)
The plan should never over or underestimate the available capacity
The MPS will inform the operations manager in very broad terms about what needs to be produced. This broad plan can include: families of product, standard hours required for jobs, and the monetary value of the orders

## Slide 18: MPS
Like any plan, it will also specify the inputs required to fulfil the plan
Inputs include: labour availability, capacity, demand from customers, and financial inputs
All planning has to have a time period attached to it to be effective
In most instances, master production planning is done in weeks
The time periods used in this planning are known as time buckets or time fences. These dates specified by management beyond which no changes to the MPS will be allowed

## Slide 19: MPS
Even though the time period of planning is important, the most important aspect here is that these time periods should be of equal length
Therefore, a time period expressed in weeks must not be followed by a planning period expressed in months
Therefore feedback from each plan to the next must be a priority. That will ensure that changes can be made that will make a plan feasible again
This is where the strength of the MRP system lies. It can measure the feasibility of any plan minutely within the capacity constraints operating within an organisation

## Slide 20: MPS
Like any good plan, the MRP system will provide the MPS with the upper bound within which the plan must operate. It will also set the lower bound for operations
The upper bound can be seen as the best possible output that can be achieved if the plan is fully operational
The lower bound is the lowest possible level at which the plan can function and still be feasible
If all of this works in concert, the result will be the master production plan

## Slide 21: MPS
The MPS can be seen as the recipe that will inform the operations department about what needs to be manufactured
For this, an aggregate demand plan is required. The aggregate plan is the demand for all the products of an organisation: therefore it shows the gross requirements for all the products of the organisation

## Slide 22: Bill of Materials (BOM)
A BOM is also known as a product structure tree
The BOM is a list that contains all the items that are needed to build one item of a finished product
The BOM must contain all items, whether manufactured by the organisation or bought from outside suppliers
The result will be that each finished product that is produced by an organisation will have its own BOM

## Slide 23: Bill of Materials (BOM)
In an organisation that does not have an MRP system there might be a BOM for engineering department, a BOM for the production department, and a BOM for the accounting department
In an MRP system, only one BOM is allowed
The BOM is an up-to-date, computerised list of all material requirements
In any MRP system, the BOM is the first hurdle that an organisation must overcome. In theory, this may sound an easy thing to do. In practice, however, the story is completely different

## Slide 24: Bill of Materials (BOM)
The larger the product becomes, the greater is the number of parts needed to assemble the product
This can result in a very large and cumbersome structure. Without a BOM the MRP system cannot operate
What is sometimes forgotten is that all part numbers that have become obsolete or redundant should be removed from the BOM and the computer system that drives the MRP system. If they are not removed, incorrect calculations will be done for the parts required to produce one complete item

## Slide 25: Bill of Materials (BOM)
S (1)
B (1)
F (1)
TC (1)
T (1)
P (6)
O (1)
S (6)
FC (1)
S (8)
R (1)
BP (1)
D (1)
W (1)
L (1)
E (2)
H (1)
A Bill of Materials or product
structure tree

## Slide 26: Bill of Materials (BOM)
It is important to understand that each of the parts listed on the BOM feature at a certain level
- At level zero the finished product is found
- At level one all the assemblies are found
- At level three all the raw materials are
found

## Slide 27: Bill of Materials (BOM)
A problem may arise when a new product is to be launched onto the market
In the majority of these cases, a BOM is not drawn up. The reason for this is that there is always a rush to get the new product onto the market before competitors can offer competing products
If the BOM is drawn up before the launch this haste may cause the BOM to be full of errors or to be incomplete

## Slide 28: Bill of Materials (BOM)
To rectify the omissions, an engineering notice with the correct information must be raised
An engineering notice is a document that will be forwarded to production to inform it about design changes that have been made
A BOM is also a very useful tool in determining the cost of a product. In some organisations, the BOM is also known as a pick list. It is called a pick list because the parts required to manufacture will be picked from inventory according to this list

## Slide 29: Modular BOM
Modular BOMs are used for products with modular designs. Modular design entails that all the parts or components required to manufacture an organisation’s products can be subdivided into modules that are easily interchangeable or replaced when this required
Modules are never the final products to be sold. These modules are used instead to assemble a final product
Modular BOMs are popular because they reduce the number of components to be scheduled to a few, instead of many
These modules can be scheduled so that various models of a stove can be manufactured using the same modules. Again, the scheduling in the MPS is simplified

## Slide 30: Phantom and Planning Bills
A planning bill is used during the planning stage of a product. Because the product does not yet exist, an artificial parent is created for the product
There are two basic situations in which a planning bill is used
When production planning is done so that assemblies and sub-assemblies can be grouped together to reduce the actual number of parts to be scheduled
When an organisation issues parts in kit form so that the product can be assembled

## Slide 31: Phantom Bills
A phantom bill is created for sub-assemblies that are not used on a sufficiently regular basis to justify their own BOMs. Therefore a phantom BOM is usually used for sub-assemblies that exist on a temporary basis
This type of sub-assembly usually forms part of another assembly and is rarely taken into inventory
The phantom parts are part of the original parent part. Phantom bills are sometimes referred to by managers as K bills or kit bills; this is because parts are issued to the production department in kit form

## Slide 32: Inventory Status File
Accurate inventory records are the third input of any MRP system. Inventory records are the stored information regarding the status of all items required by a specific time period or in a time bucket
The following will be included in the time bucket:
- gross requirements for each part
- scheduled receipt date of the material
- stock on hand in the warehouse or store
Other information that might be included is the name of the supplier, the lead-time, and the sizes of the lots to be produced
All the above information is required to ensure a correct material availability status

## Slide 33: Inventory Status File
Changes to stock levels due to withdrawals, cancelled orders or any other event then also require an accurate inventory record
Without a superb inventory system, an organisation will find it nearly impossible to install an MRP system
The inventory records form the lifeblood of the MRP system. In the traditional system, inventory accuracy is ensured by periodic stock checks or counts
This type of practice is not nearly accurate enough for an MRP system. If managers tamper with the integrity of the inventory, they will have a sick MRP system on their hands

## Slide 34: Inventory Status File
In MRP organisations, cycle counting has been developed to replace the yearly stock count
According to this method, a small number of different stock items is counted over a time period
For example the number of working days, and then the number to be cycle counted will be arrived at

## Slide 35: Inventory Status File
An organisation has 5,000 items in stock and works 200 days per year
Therefore the items to be cycle counted per day is
5000 / 200 = 25 per day

## Slide 36: Inventory Status File
Inventory records cannot be complete if an organisation does not know what material is outstanding on purchasing orders
The operations department should have access to the delivery dates of all purchased orders
It is also important for the operations department to know when the orders were placed. This information is required to ensure the proper planning of manufacturing
A lack of this information means poor planning and an ineffective MRP system. The production plan will therefore not be executed as planned

## Slide 37: Inventory Status File
This lead-time of the material will determine to a great extent the delivery data of the finished product
An operations department not only needs the lead-time for purchased goods but also that for produced and assembled parts
What constitutes a lead-time? Lead-time for purchased material is from the day the firm order is placed with supplier until delivery of the ordered material has taken place
Lead-time in an operations department includes the time to deliver material between work centres, machines, and departments, the set-up times of machines, the assembly time of the product and the run times

## Slide 38: Inventory Status File
Run time is the time taken, excluding set-up time, to complete the process at a specific machine
If all this information is included in BOM, this BOM becomes what is known as a time phased product structure tree
In a time phased product structure tree the times required to build the finished product are included in the structure

## Slide 39: Inventory Status File
The impact of incorrect lead times on the planning and execution of an MRP system can be just as devastating as that of incorrect inventory levels
The MRP system has three main file where the records for inventory will be kept. They are:
Item master file
The transaction file
The location file

## Slide 40
MPS input
Forecast Demand
Records of inventory
Orders from customers
Works orders
Materials plans
Bought out items
The MRP System
BOM
Records for inventory in an MRP system

## Slide 41: Item Master File
Contains information such as on-hand inventory, quantities on order, lot sizes, safety stock to be held, lead times, and previous usage rates

## Slide 42: Transaction File
For the MRP system to function optimally, the system must know the level of the stock holding for each particular part number
This means that the computer must know at all times what quantity of an item is available for use
The transaction file keeps records of the receipt of orders, issues to the shop floor of parts, and the available balance for use
Information in the transaction file is updated as the transaction takes place. When items are received from the supplier, the system is updated as the stock is received. The same happens with stock withdrawals from inventory

## Slide 43: The Location File
Like any department in an organisation, a warehouse also needs to be managed properly
Most organisations use fixed bin systems for storing inventory. A part number is always allocated a bin number and that particular part is always stored in that bin
This system might not be ideal for organisations with ever-changing parts. In these cases, random bin systems are employed
Every time a new part is received, the computer makes a decision regarding the bin in which that particular part is to be stored

## Slide 44: The Location File
The random method must be carefully managed because the same part number might be stored at various locations in the warehouse.
An important advantage of this system is that stock turnover can be better managed by making use of the first in/first out principle
This system can also assist with better utilisation of the space in the warehouse

## Slide 45: Structure of an MRP System
The preceding discussion has shown that, for an organisation to have a genuine MRP system, it needs an MPS, a BOM, records for inventory and purchasing, and the lead times for each item
Once accurate information is available, the gross requirements for an item can be determined
The MRP system uses the information contained in the MPS and explodes it into the time phased requirements for things such as assemblies, parts and raw materials
The exploded bill of material quantities is known as the gross requirements

## Slide 46: Structure of an MRP System
The gross requirements are the total demand that can be expected for any item or raw material in a predetermined time period
It is important to note that the gross requirement plan’s departure point is that there is no inventory available
The assumption therefore is that there will be purchased orders
On the other hand, the net requirement plan uses the assumption that there is some inventory available

## Slide 47: Structure of an MRP System
The net requirement plan will accentuate the requirements of the material the organisation will actually require
Using this type of plan will enable an operations manager to determine what material has been allocated to which jobs but not yet been used
This type of inventory is known as allocated inventory. Allocated inventory is inventory that can be used only for the job to which it has been allocated
To simplify the whole process as described above, the assumption is made that no safety will be included

## Slide 48: Structure of an MRP System
Planned-order releases determines the sizes and timing of orders
Planned-order releases is the amount of an item that the organisation plans to order in a specific period. The total in this instance is derived from the planned-order receipts minus the lead-time for delivery
The amount of an item that the organisation plans to order in a specific period maybe a fixed quantity or an order quantity that will cover the exact quantity that is required at that specific time
These two types of order quantities are most widely used in industry. The timing of the receipts of the quantities specified in planned-order releases is shown by planned order receipts

## Slide 49: Structure of an MRP System
Gross requirements: - this is the total demand that can be expected for any item or raw materials in a predetermined time period
Scheduled receipts: - these are the open orders still outstanding. This means the orders have been placed at suppliers but not yet received. These quantities will be received at the beginning of a production period
Project on hand: - this quantity is the expected amount of any item that will be available at the beginning of a specific period. These quantities are made from scheduled receipts and any inventory left over from the previous period

## Slide 50: Structure of an MRP System
Net requirements: - this is the exact amount of an item that will be needed in a specific time period
Planned-order receipts: - this is the amount of material expected to be received at the beginning of the time period in which it is required
If lot-for-lot ordering: - is used, the quantity will be the exact amount required. That means that it will meet the net requirements for that item
If Lot sizing is used, the planned-order receipts might exceed the net requirements. In this case, a predetermined order quantity is ordered

## Slide 51: Outputs of an MRP System
Certain information is produced if an organisation uses an MRP system
The MRP system’s outputs are classified into two types of reports
Primary reports: - these are the main reports produced
Secondary reports: - these are the optional reports produced

## Slide 52: Primary Reports
The planning and control of production and inventory forms part of the primary reports
Therefore the outputs of the MRP system dynamically provide the schedules for future material usage
To ensure effective reporting, the primary reports should contain the following information:
Change report: - this details all the changes that can be done to existing orders. These changes include changes to due dates (delivery dates) and quantities ordered and cancellations by customers

## Slide 53: Primary Reports
2. Orders planned: - this report provides information regarding the number of orders. The report will include the quantities of the orders as well as the dates by which these orders should be delivered
3. Orders released: - is not a report in the true sense. This type of report is the authorisation to start work on any particular order. No order can be launched onto the shop floor without the authorisation of this report

## Slide 54: Secondary Reports
All reports that deal with measuring the performance of control mechanisms and performance of the planning process and exception reports are classed as secondary reports
The following are some of the most frequently used secondary reports
Reports concerning performance control: - this type of report will evaluate the performance of the system as a whole
By using this type of report, operations managers can measure any deviation from the plan

## Slide 55: Secondary Reports
Reports concerning performance control: - typical deviations that will be highlighted are delivery dates not met, stock-outs that did occur, deviations from performance standards, and deviations from the required number of stockturns
Cost performance can also be measured by using this type of report
Reports for planning: - these types of report are used in the forecasting of future inventory demand. This will include the forecasting of future purchased orders as well as data that will be used to assess material requirements in the future
Exception reports: - these types of report highlight any major deviation from what has been planned. These exceptions might include, late deliveries or orders, overdue orders, unacceptably high scrap rates, errors in planning, and orders placed for non-existent parts

## Slide 56: Safety Stock
As a result of having an effective MRP system, no organisation with dependent demand should hold safety stock below the finished product level.
The reason for this is that the operations manager should be able to predict precisely what the average usage rate will be for all items needed to produce the final product
In any real situation, there may be exceptions. Somewhere in a process a bottleneck may occur
A bottleneck occurs if items in the manufacturing process collect at a work centre and are processed much more slowly than in the rest of the process

## Slide 57: Safety Stock
This results in shortages of the item further down the process; the work centres following the bottleneck might run out of work and therefore be idle
The same situation may arise if raw material is received late or it takes longer than expected to assemble or manufacture an item
This situation may tempt an operations manager to make use of safety stock. Any advantages gained by using an MRP system can be lost if a process keeps safety stock

## Slide 58: Safety Sock
It is possible for an MRP system to deal with these problems by:
Identify the work centre (s) influenced by variability in their performance
Determine the full extent of the variability

## Slide 59: Safety Stock
As an example, assume that it is the lead time that varies. Instead of making use of safety stock, the operations manager can use safety time
Safety time entails scheduling of the items subject to variability well in advance of the required date; this will ensure that the items are delivered as promised, irrespective of the variability they face
The result is that the chance involved in the whole process can be eliminated or at least properly managed
The carrying of small quantities of safety stock may be permitted if the variability influences quantities

## Slide 60: Safety Stock
Lead-times need to be very accurate because many of these shortages are caused by incorrect lead-times
This is especially true if parts and raw materials are received shortly before they are required in the manufacturing process
If the organisation receives the shipment too early, inventory holding cost will increase
If it receives the stock late, this may cause mayhem in the whole manufacturing process and result in late deliveries to customers

## Slide 61: Safety Stock
Each of these situations carries its own monetary penalties
Some managers tend to inflate the lead-time to counteract late deliveries. If this is done the purpose of MRP system- namely to have the correct material available at the correct time- is defeated
Safety stock can be accommodated by increasing the quantities of the planned- order releases for items to be produced

## Slide 62: Lot Sizes
Lot sizing is selecting the optimal size of a batch of products to be manufactured to meet the requirements of the process
In inventory management this issue is of great importance and is applicable to both dependent and independent demand
In most cases managers will use EOQs or EPQs as the lot size to be produced or purchased for independent demand items
The types of plan unfortunately do not work for dependent demand items. A greater variety of plans is required to determine the lot sizes in this instance

## Slide 63: Lot Sizes
For every order placed by an organisation, costs are incurred. It is important that these costs are minimised by the inventory system used by the organisation
Independent demand, as a rule, is evenly distributed through any planning horizon. This is not the case with dependent demand, which is lumpier
Dependent demand occurs in a much shorter time horizon than independent demand. For this reason, a manager may find it more difficult to calculate the economic order quantities for this type of demand

## Slide 64: Lot Sizes
One way for managers to ensure economies of scale for ordering is by grouping orders together
The reason for this is that savings achieved in the set-up and ordering costs can offset the cost of holding the extra stock
The calculation of this saving is not easily achieved. There are various reasons for this:

## Slide 65: Lot Sizes
If orders are lumped together in a single order, this will have a cascading effect throughout the product structure tree
This can be countered if the demand of lower-level items is grouped together and their set-up time and holding costs form part of the decision
Due to the fact that the planning horizon is shorter for this type of item, lot sizes must be re-calculated more often
In addition, this type of demand is uneven. For this reason, the methods used to determine lot sizes vary from the very complex to the easy to understand and use

## Slide 66: Lot-for-Lot Ordering
Method
This type of calculation is the simplest and easiest to use
The demand for an item in a certain period will then automatically become the lot size for that item in that particular time frame. For example, if the demand for an item is 150 units in a certain time period, then the lot size for that item will be 150 units

## Slide 67: Lot-for-Lot Ordering
Considerations
The major advantage of this type of ordering is that holding cost for an item is virtually eliminated. The minimisation that inventory systems strive for has been achieved in using this method
All is not plain sailing in using this method. Because this method uses a fixed quantity it is difficult to nearly impossible to take advantage of the economics of fixed order sizes. Also, the production costs to produce these items increase because set-up costs are incurred every time these items have to be produced

## Slide 68: Economic Order Quantity (EOQ)
Method
When the usage for a specific item is uniform, costs can be minimised by using this model
This model is mostly used for determining order sizes for lower-level items of specific parent items and determining the order sizes for raw materials

## Slide 69: Economic Order Quantity (EOQ)
Considerations
The main drawback in using this method is that the lumpier demand becomes, the less likely it is that this method can be used
Demand for end items is usually the lumpiest of all demand and the use of EOQ model is less likely for this type of demand

## Slide 70: Fixed Period Ordering
Method
When pre-determined number of periods is used, this is the method used to calculate lot sizes
Mostly the span of the time period is set arbitrarily by management
To have a more reliable fixed time period span, historical data can be analysed

## Slide 71: Fixed Period Ordering
Consideration
A rule of thumb that is often employed is a two-week fixed time span period for ordering

## Slide 72: The Management of an MRP System
It can never be said that an MRP system is static or never changes. In most organisations, the route being followed involves greater integration of MRP and JIT systems

## Slide 73: The Dynamics of MRP
When changes occur in the design of a product or in the schedules for items and production processes, the BOM and MRP must also be changed
Whenever a change occurs in the MPS, that change must also be reflected in the materials plan
Manipulation of the MRP system can be undertaken, regardless of the reasons behind the changes and therefore, the MRP can reflect any change
As a result of this manipulation, it is a common practice for managers to re-calculate the materials plan at least once a week

## Slide 74: The Dynamics of MRP
It is possible to achieve a timely and accurate re-planning of the MRP of the MRP system because this is an inherent feature of the MRP system
Many organisations do not re-plan their materials plan if only small changes take place over time. If too many changes are made to the materials plan, it develops what is known as system nervousness
System nervousness will create chaos in the purchasing department as well as production if all the small changes that do occur are implemented

## Slide 75: System Nervousness
There are two basic methods that can be used to prevent system nervousness:
Times fences designate a certain portion of the master production schedule as not to be re-scheduled. For example, the time fence will prohibit re-scheduling of the MPS for the first three weeks of that schedule. Therefore, that time period will not be taken into account when the MPS is re-scheduled. The result will be that there will be certainty about what is required of the purchasing and production departments for that three-week period

## Slide 76: System Nervousness
2. Pegging is upward bracing of materials and components in the BOM from the lower levels to the parent part to enable the planner to determine the reasons behind any changes in requirements and whether or not these changes should be included in the schedule

## Slide 77: Advantages of an MRP System
Stock will be turned over on a regular basis
Demand is known and therefore materials are linked to the demand
There are no delays in the delivery of materials and better customer service results
Saving in space, capital warehousing etc. can be achieved because of lower stock levels
Delivery dates of materials and finished goods are more reliable and quicker

## Slide 78: Advantages of an MRP System
Better planning is encouraged
Short-term planning can be done more effectively
Because materials are available, facilities can be optimally utilised
Expediting of orders is required and less emergency orders for stocked-out materials have to be placed

## Slide 79: Disadvantages of an MRP System
Scheduling of production using the MRP system can induce poor performance results
Capacity and other constraints may not be recognised by the system
The system is not very flexible in dealing with changes
Large amounts of detailed, reliable information are required
In real time, the sequence in which parts are manufactured differs from what is specified in the BOM

## Slide 80: Disadvantages of an MRP System
Inefficient lot sizes are specified
Implementation of the system requires a large amount of time and money
The longer the system is used, the more complex it becomes
A large amount of data must be manipulated on a regular basis

## Slide 81: JIT and MRP
The wide acceptance of the JIT principles and techniques came in the 1980’s, after many manufacturing operations had made use of the MRP-based systems
The operating philosophies of MRP and JIT do seem to be fundamentally opposite. JIT encourages a ‘pull’ system of planning and control, whereas MRP is a ‘push’ system
JIT has aims which are wider than the operations planning and control activity, whereas MRP is essentially a planning and control ‘calculation mechanism’

## Slide 82: JIT and MRP
Key Characteristics of MRP
Although designed as a pull system, the way MRP works is to drive inventory through each process in response to detailed, time-phased plans, calculated by part numbers
MRP is highly dependent on the accuracy of data derived from bills of materials stock records, and so on
MRP systems assume a fixed operations environment, with fixed leads which are used to calculate when materials should arrive at the next operation
However, loading conditions and other factors mean that lead times are in reality far from fixed

## Slide 83: JIT and MRP
Key Characteristics of JIT
The flow between each stage in the manufacturing process is ‘pulled’ by demand from the previous stage
The control of the pull between stages is accomplished by using simple cards, empty squares or tokens to trigger movements and production
Decision-making for operations control is largely decentralised: tactical decisions do not rely on computer-based information processing
JIT scheduling is ‘rate-based’ rather than volume-based

## Slide 84: JIT and MRP
Key characteristics of JIT
JIT assumes resource flexibility and minimised lead times
JIT planning and control concepts are only one part of a wider and explicit JIT philosophy of operations

## Slide 85: Balanced Flow Approach
The MRP system will support planning and scheduling in a repetitive manufacturing environment
For the balanced approach to function, properly, the MRP systems planning portion must be merged with the JIT principles
The JIT system will make use of kanbans and visual signals to pull material through the facility rather than using the push system

## Slide 86: JIT and MRP Similarities
MRP seeks to meet projected demand by directing that parts and sub-assemblies are only produced as needed to meet that demand
MRP back schedules demand for parts and sub-assemblies by using the bill of materials to calculate how many are needed and when they must be made
This is how MRP connects customer demand with the internal and external supply network while JIT planning and control has similar objectives
Pull scheduling aims to connect the new network of internal and external supply processes so that parts only move in response to co-ordinated and synchronised signals derived from end-customer demand

## Slide 87: JIT and MRP Differences
MRP is driven by the master production schedule, which identifies future end-item demand
It models a fixed lead-time environment, using computer to calculate how many of, and when each part should be made
Its output is in the form of time-phased requirements plans that are centrally calculated and co-ordinated. While MRP is excellent at planning, it is weak at control
On the other hand, JIT-style pull scheduling aims to meet demand instantaneously through the use of kanbans

## Slide 88: JIT and MRP Differences
In practice the actual throughput time of which the system is capable must be recognised. If the total throughput time (P) is less than the demand lead time (D), then the JIT system should be capable of meeting demand
Pull scheduling is a reactive concept that works best when independent demand has been levelled and dependent demand synchronised
While JIT may be good at control, it is weak on planning

## Slide 89: JIT and MRP Differences
MRP is better at dealing with complexity, as measured by number of parts and finished products
It can handle detailed parts requirements even for products that are made infrequently and in low volumes (‘strangers’)
JIT pull scheduling is less capable of responding instantaneously to changes in demand as the part count, options and colours increase

## Slide 90: JIT and MRP Differences
Therefore, JIT production systems favour designs based on simpler product structures with high parts commonality
Such disciplines challenge needless complexity, so that more parts may be brought under pull-scheduling control