## Slide 1: Computer Architecture & OS ACCA4022
Week 5: Fundamentals of Logic Gates

## Slide 2: Recap
In the previous session, we :
described a number system
Converted a number from one number system to a different number system
Represented numbers in decimal, binary, octal, hexadecimal
Performed basic arithmetic (+, -,*) on binary numbers

## Slide 3: Activity 11
Perform the following calculations and post your answers on the shared whiteboard
(1DA)16 2. (306)16
Decimal
Binary
Octal
3. (653)8 (653)8
Decimal
Binary
hexadecimal
5. (653)10 (897)10
Binary
Octal
hexadecimal

## Slide 4: Objectives
By the end of this session, students should be able to:
describe a logic gate and logic circuit
Construct a logic circuit and its truth table
Identify different logic gates in a circuit
Identify output of a given circuit

## Slide 5: Logic gates
Logic gates are building blocks of any digital system used to create digital circuits and perform binary computations
logic gates are used in the creation of complex circuits like multiplexers, demultiplexers, encoders, decoders, and arithmetic logic units (ALUs).
They are used to control the flow of information, create complex circuits, and understand how computers work.
A logic gate is a series of transistors connected together to give one or more outputs, each output determined by the input or combination of inputs.
It is an electronic circuit having one or more than one input and only one output.

## Slide 6: Logic gate
Most logic gates accept an input of two binary values and provide an output of a single binary value.
Every terminal in a logic gate will always be in one of the two binary states which represent the presence or absence of an electric voltage.
Logic gate states | 
Presence | Absence
1 | 0
ON | OFF
Positive | Negative

## Slide 7: Logic gates
These are basic types of logic gates each performing a specific logical operation.
1. AND gate
2. OR gate
3. NOT gate
4. NAND gate
5. NOR gate
6. XOR gate
7. XNOR gate
We use a truth table to show the possible inputs and the resulting output
An output of one logic gate can be an input to another logic gate.
Notes: NB: It is important to understand how each logic gate works so that you may also determine the output of a circuit.

## Slide 8: Truth tables
It is a table used to compute the functional values of logical expressions on each combination of values taken by their logical variables.
A convenient way to visualize the outputs for the logic gates is through a truth table
• The truth table depicts the gate’s response to each possible set of inputs
Useful to show the state after each logic gate on the truth table.
Notes: A truth table is a mathematical table used in logic to compute the functional values of logical expressions on each of their functional arguments, that is, on each combination of values taken by their logical variables.
Truth tables are a convenient and comprehensive method to illustrate how binary inputs will influence the output of a particular gate or an entire logic circuit. They help verify the correctness of a logic circuit, no matter how intricate it may be.

## Slide 9: AND gate
AND gate: takes two inputs and produces one output
Only two positive inputs (1) and (1) will result in a positive output (1)
Here, output would be Z, where value of Z would be Z = A AND B or (A.B)
Both inputs must be positive (1) for the output to be also positive (1)
Input A | Input B | Output Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: The AND gate takes two inputs and produces one output
Only two positive inputs (1 and 1) will result in a positive output of 1
If either of the inputs is a 0 the output will be a 0
A AND B or Q = a.b

## Slide 10: OR gate
2. OR gate: Takes two inputs and produces one output.
If either of the inputs is positive (1) the output will be positive(1)
Here, output would be Z, where value of Z would be Z = A OR B or (A+B)
At least one input has to be positive (1) to give a positive output (1 or ON). Both inputs could also be positive to give a positive output
Input A | Input B | Output Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Notes: The OR gate takes two inputs and produces one output
If either of the inputs is positive (1) the output will be 1
OR also needs two inputs
• OR needs one input to be ON for it to spit out ON • It is also ON when both inputs are ON • It is OFF when both inputs are OFF
OR B or X = a + b

## Slide 11: NOT gate
3. NOT gate: Inverse the current output, therefore, positive (1 or ON) becomes negative (0 or OFF), whilst negative (0 or OFF) would become positive (1 or ON)
Here, output would be Z, where value of Z would be Z = A
The NOT gate takes a single binary input and outputs the opposite of the input
Input A | Output Z
0 | 1
1 | 0
Notes: NOT A or Q = ā

## Slide 12: NAND gate
4. NAND gate: Not AND. Is a combination of an AND gate followed by a NOT gate.
If both inputs are a 1 it will output a 0. Any other combination of inputs will result in an output of 1
Here, output would be Z, where value of Z would be Z = A NAND B or (AB)
Input A | Input B | AB | Output Z = AB
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: A NAND B or Y=a-.b-

## Slide 13: NOR gate
5. NOR gate: NOT OR. A combination of an OR gate followed by a NOT gate
If both inputs are 0 it will output a 1, any other combination of inputs will result in an output of 0
Here, output would be Z, where value of Z would be Z = A NOR B or (A+B)
The same as OR gate, but then inverse (NOT) the outcome. So, perform OR first, then apply a NOT to the output
Input A | Input B | A+B | Output Z = A+B
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: A NOR gate is a combination of an OR gate followed by a NOT gate. If both inputs are 0 it will output a 1. Any other combination of inputs will result in an output of 0
A NOR B or Z=a- + b-

## Slide 14: XOR gate
6. XOR gate: Exclusive OR. XOR will output positive (1) if the inputs are different from the other (a 1 and a 0)
Here, output would be Z, where value of Z would be Z = A XOR B
Only one input is allowed to be positive (1 or ON) to give a positive output (1). If both inputs are positive (1), then there is a negative outcome (0, or OFF)
Input A | Input B | A | B | A.B | A.B | Output Z = A.B + A.B
0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0
Notes: XOR is the short way to say “Exclusive OR” • Like OR, XOR also only needs one input to be ON for it to spit out ON • But unlike OR, when both inputs are ON, XOR spits out OFF • It is also OFF when both inputs are OFF
XOR B or Y = (a.b-)+(a-.b)

## Slide 15: XNOR gate
7. XNOR gate: Exclusive NOR. XNOR will output positive (1) when both inputs are the same and false if the inputs are different.
The output is the inverse of that of XOR gate
Here output Z = A XNOR B
Input A | Input B | Output Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: XOR followed by NOT: True if A and B are both True or both False
Z = A XNOR B
An XNOR Gate Is A Digital Logic Gate That Outputs True Or '1' Only When All Inputs Are True Or '1its output is the inverse or 'NOT' of that of an XOR gate.
An XNOR gate outputs true or '1' only when the number of true inputs is even, its output is the inverse of an XOR gate.
The XNOR gate's truth table makes clear that the output is 'true' or '1' only when both inputs are the same, hence the term 'equivalence gate'.

## Slide 16: Summary Logic Gates
Logic gates (madpcb, 2024)

## Slide 17: Logic circuits
Logic circuits are designed to perform a particular function
When logic gates are connected, they form a Logic circuit where the output from one gate is used as input to the next connecting gate
Which of the logic gates can you identify from the given circuit?

## Slide 18: Methods of Creating Logic Circuit Truth Table
On the circuit diagram, add temporary letters after each gate (C, D, E, etc. )
Create a blank truth table, allowing space for all the temporary letters (stages)
Write into the truth table all the possible unique input combinations (A and B combinations for example)
In the truth table, calculate the output at each temporary letter, treating them as separate mini logic problems (e.g. D is the result of A OR B)
Eventually you will reach a stage where you are able to find the final output for the logic circuit (Z for example)

## Slide 19: Creating Logic Circuit Truth Table Example

## Slide 20: Logic Gates - Exercise
1. Based on the discussions above, create a truth table for the following logic circuit

## Slide 21: Logic Gates – Exercise Solution
1. Based on the logic circuit above, create a truth table for the following logic circuit
Input A | Input B | Y=A- | X=A+B | D=XY | Z=D+X
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1

## Slide 22: Logic Gates - Exercise
2. Based on the logic circuit below, create a truth table

## Slide 23: Logic Gates – Exercise Solution
2. Based on the logic circuit (on slide 17), create a truth table

## Slide 24: Logic Gates - Exercise
3. Draw logic circuits and create truth tables based on the below output:
Z = Y.X + X
Z = AB + CD.C

## Slide 25: Activity 12
In pairs , access Activity 12 on Moodle and attempt all questions.
Share your answers with the class.

## Slide 26: References
V. Vijayendran, Fundamentals of Microprocessor – 8085, Chennai: S. Viswanathan (Printers & Publishers), PVT. LTD, 2004
W. Stallings, Computer Organisation and Architecture, London: Pearson, 2016
I. Englander, The architecture of Computer Hardware, Systems Software & Networking – An Information Technology Approach, London: John Wiley & Sons, 2014
Khan Academy Logic circuits [online] available https://www.khanacademy.org/computing/computers-and-internet/xcae6f4a7ff015e7d:computers/xcae6f4a7ff015e7d:logic-gates-and-circuits/a/logic-circuits, 2024
MADPCB Logic gate [online] available https://madpcb.com/glossary/logic-gate , 2024

## Slide 27: Next lesson
Storage Technologies
Week 7 – in class mock test
All that we have covered