## Slide 1: Starship Material Selection
Level 5 Group Project – ACMA5009
Notes: Welcome to my video presentation on Starship material selection

## Slide 2: Contents
Introduction
Materials in Service
Operating Environment
Material Properties
Advantages Gained
Overcoming High Density
Manufacturing
Summary
Notes: The contents of this presentation include…..

## Slide 3: Introduction

## Slide 4
Starship will be the largest and most powerful launch vehicle ever produced
Originally designed as the first all carbon fiber rocket body
Engineers redesigned the plans and opted to use 301 stainless steel for starship
This decision shocked many engineers/ scientists globally due to stainless steels high density

## Slide 5: Materials In Service
Notes: This section will cover the materials used to manufacture rocket bodies, looking at the past present and future.

## Slide 6: Stainless steel
Early rockets were designed and manufactured using stainless steel
S/S high density forced engineers to make bold design features to minimise the weight
Balloon tanks – Atlas V rocket
WD40 – displace the water on rockets surface
Engineers needed to design around the limitations of the material
This was not the best material, but the best engineers had at the time
Notes: Balloon tanks required positive pressure to maintain structural integrity when vertical.

## Slide 7: Aluminium alloys
Advances in manufacturing techniques and metallurgy processes paved the way for lighter materials
Alloying with lithium created a lighter and higher strength material
Space shuttle saved an estimated 3600Kg of weight
SpaceX Falcon 9 rocket body produced out of lithium alloys
Lower melting temperatures meant it required heat protection tiles

## Slide 8: Carbon fiber composites
High strength low density gives it significant advantage over other materials
Prone to imperfections
Difficult to machine
High cost with large amount of waste
Advances in manufacturing techniques will need to be made

## Slide 9: Operating environment
Notes: Prior to looking at the material selection process it is important for us to understand the operating environment that these rockets will be exposed to. Space puts all materials under severe conditions allowing only the most robust to survive. Temperature, gravity, and corrosion are just a few variables not experienced as they are on earth. The material selection needs to be robust enough to withstand this environment.

## Slide 10: Temperature
Large temperature variations experienced when travelling through space.
Approx 300˚C when sun side in low earth orbit
Extreme heat generated by friction when passing through earths atmosphere
Freezing cold conditions also experienced down to cryogenic temperatures

## Slide 11: Gravity
On take-off the spacecraft needs to overcome earths gravitational pull
During launch these forces will be magnified up to three times the force on earth
Materials should not deform under these forces and needs to maintain its integrity
Weight of the rocket can have a significant impact on these forces making it important to keep weight low

## Slide 12: Corrosive
We associate the near perfect vacuum of space to eliminate the effects of corrosion
The onboard systems will produce and expel particles and gasses in the vicinity of the spacecraft
Creating an induced environment around the spacecraft
Materials need to be durable and withstand the effects

## Slide 13: Material Properties (Stainless Steel)

## Slide 14: 301 STAINLESS STEEL
301 Stainless steel has high melting point and can withstand extreme heat
The nickel and iron give it excellent ductility and heat resistance
The high chromium content of up to 18% gives it excellent thermal properties
301 Stainless steel is a Nickel, Chromium, Iron blend with a low carbon content which gives it these properties

## Slide 15: 301 stainless steel
A unique property of stainless steel is its ability to withstand low temperatures while maintaining good strength
Many metals become brittle at cryogenic temperatures but this is not the case for stainless steel
Stainless steel becomes stronger and more ductile at low temperatures
This unusual material property gives it an advantage over other materials

## Slide 16: Advantages Gained

## Slide 17: Cost
Cost was one of the main factors driving SpaceX to stainless steel
Stainless steel is over 50 times cheaper to purchase over carbon fibre
35% of carbon fibre is wasted when cut for manufacturing purposes increasing the cost to purchase and inducing further waste
Stainless steel is available to purchase further reducing manufacturing costs

## Slide 18: Strength/durability
One of the biggest advantages of using Stainless steel is the materials overall strength
Maintains strength at very high and extremely low temperatures
Many metals become brittle at cryogenic temperatures
Stainless steel is unique as it becomes stronger and more ductile at cryogenic temperatures

## Slide 19: Availability
Stainless steel can be simply purchased off the shelf in a variety of sizes
It is available in 1.8M rolls suitable for 9M diameter sections
Carbon fibre required complex processing and manufacturing techniques making it difficult to produce large sections
This availability allowed SpaceX to start producing prototypes immediately

## Slide 20: OVERCOMING Stainless steel high density

## Slide 21: RAPTOR Engines
To build a large rocket with a higher density material you will need an engine with a greater amount of thrust
Raptor engine currently offers double the amount of thrust for the same size engine used on Falcon 9 (Merlin).
Raptor Engine uses liquid oxygen and methane as propellent, this burns clean compared to other fuel types
Increasing its reusability and reducing the amount of maintenance needed between missions
Liquid oxygen is stored at cryogenic temperatures, stainless steel becomes stronger at these temperatures.

## Slide 22: Heat protection
Traditionally spacecrafts have been fitted with ceramic heat protection tiles.
These tiles are essential to prevent space rocket burning up as they pass through Earths thick atmosphere
Heat protection would add significant weight to the launch vehicle
The tiles on re-entry would suffer significant damage and needed replacing with costly and time-consuming maintenance periods
The switch to Stainless steel allowed them to rethink the heat protection system, due to stainless steels weldability meant they could weld stringers creating an outer and inner surface
liquid methane will flow between the layers on re-entry with the outer layer having micropores which will sweat liquid methane onto the surface, cooling the underside
By removing the need for heat protection tiles will not only reduce the weight of the rocket but also improve its strength when vertical

## Slide 23: Manufacturing

## Slide 24: Machinability/bonding
Stainless steel is easily bonded using simple welding techniques
Easy to machine and can withstand small structural imperfections such as cracks
This change has simplified the manufacturing processes saving time and resources
Since the switch SpaceX has been able to manufacture prototypes quickly
Carbon fiber in contrast is prone to imperfections and very difficult to machine, ultimately the reason behind SpaceX abandoning the original design

## Slide 25: Cold Rolling
Since stainless steel was used in the 1960’s manufacturing processes have improved
Cold rolling technology has developed and allows for stainless steel to be manufactured to extremely fine tolerances
The material at cooler temperatures requires greater forces to deform the material, this deformation produces material with a higher strength to weight ratio
This process manufactures material with better surface finish, increasing its resistance to corrosion.
SpaceX aims to enhance this by cold rolling at cryogenic temperatures, thus further increasing the material strength to weight ratio

## Slide 26: Low-cost prototypes
The switch to using stainless steel allowed SpaceX to dramatically reduce the cost to build Starship prototypes
SpaceX due to the low cost adopted the iterative design process
Rockets are built quickly, tested, data collected, modified, and retested
This basic principle allows them to continuously evolve the design and conduct physical tests of the conceptual design
This principle would not be possible if using expensive materials such as carbon composites

## Slide 27: Summary

## Slide 28: Summary
Strength to weight performance – Lithium alloys
Stainless steel strength to temperature performance
Design features helped reduce the overall rocket mass
Main advantage is cost and availability
Simple manufacturing techniques sped up the process
Able to develop prototypes quickly
Difficulties with carbon fiber – manufacturing times / prone to imperfections
Advances with manufacturing techniques improved stainless steels properties
Further advances will allow for less material and further reduce weight
Material selection influencing the design
Future of Starship
Notes: When designing space rockets designers usually favour strength to weight and mainly opt for lithium-based alloys for this reason.
SpaceX engineers saw the potential in using stainless steel, despite its greater density value it offered something different, its superior strength to temperature performance gave them a significant advantage
It allowed them to engineer design features never been considered before, in doing so help reduce the overall mass.
The cost and availability ensured ease of production and simplified the manufacturing process, with low costs and rapid production.
This allowed production of low cost prototypes, they are tested to failure providing accurate data, further speeding up the development process.
Carbon fibre proved unsuitable due to its high cost, time consuming and difficult manufacturing process which often caused imperfections, advances with manufacturing techniques will need to be made before this becomes suitable.
Cold rolling will ensure that the performance of stainless steel will be improved, including cold rolling at cryogenic temperatures. This will lower the overall weight and improve its strength.
Previously the design needed to suit the limitations of the material but stainless steel is now providing many of the solutions engineers require and has allowed new design features never seen before.
Starship is still in the very early stages with prototypes currently being developed, I expect SpaceX to make further advances with different alloys of stainless steel improving its properties, further reducing the overall mass with ingenious design features.

## Slide 29: END