## Slide 1: Ordnance, Munitions and Explosives Principles of OME Level 4 ACDA4019 Deflagration, Detonation and the Ignition Train

## Slide 2: Aim of Lecture
Consider the mechanisms for producing an explosive event, the requirements that are placed on the chemical components, and examples of explosives in military use.

## Slide 3: Start sensitive and build from there!
Match, Paper, Wood, Coal.
You wouldn’t hold a Swan Vesta under a lump of best Welsh anthracite steam coal and hope it would light? Would you?
You’d build the fire from paper, kindling, wood and then coal.

## Slide 4
EGDN
NG
TNT
H2O(g), CO2(g)
C(s), CO(g)
O2(g)
Primary and Secondary Explosives

## Slide 5
NG
NC
(14.14%)
Single Base
NC/NG
Double Base
Oxygen Balance
Force Constant
-30
-24
+3.5
0
NQ
(54.4% N)
NC/NG/NQ
(Triple Base
Propellants
NC = Nitrocullulose
NG = Nitroglycerine
NQ = Nitroguanidine
Nitroglycerine
Nitroguanidine
Nitrocellulose

## Slide 6: Ignition / Detonation Train Design

## Slide 7: To fully understand explosive chemistry, it is important first to define deflagrations and detonations and highlight the characteristics that distinguish these two types of combustion waves. Deflagration and detonation are differentiated from usual combustion by their power output, velocities of propagation (some mms-1 for combustion, several hundred ms-1 for deflagration and several thousand ms-1 for detonation), and the source of oxygen that they use.
Reaction Type | Reaction rate | Power Output | Oxygen Source | Example
Combustion | Slow (mms-1) | 100 Wcm-3 | Atmosphere | Burning Wood
Deflagration | Subsonic (+100ms-1) | 100 Wcm-3 | Within compound | Confined black powder
Detonation | Supersonic (+330ms-1) | 1000 Wcm-3 | Within compound | TNT

## Slide 8: What is deflagration
Deflagration is a rapid burning where convection plays an important role (the transfer of heat between areas of different temperature). The term is often used to describe the burning of an explosive which has failed to detonate.
Notes: The propagation of an explosion reaction through a deflagrating explosive is based on thermal reactions. A deflagrating explosive will ignite when subjected to an external stimulus such as flame, spark, shock, friction or high temperatures. Burning begins on or just above its surface, essentially receding layer by layer as one would imagine when sucking a hard boiled sweet. The rate at which the surface of the explosive burns is known as the linear burning rate, which is governed by Equation 1, where r is the linear burning rate coefficient in mms-1, P is the pressure at the surface of the explosive at a given instant in Nmm-2,  is the burning rate coefficient and  is the burning rate index.
Equation 1: Linear Burning Rate
In a deflagration reaction, the temperature of each layer of the explosive is brought to the ignition point as it recedes, with heat being radiated and conducted from the reaction zone into the solid material. The rate at which the surface recedes depends on the rate of heat transfer into the explosive, which itself is dependent upon the pressure at the surface of the composition as Equation 1 demonstrates. As such, the rate of surface regression can increase hugely if the explosive is confined (completely enclosed), since the gaseous products of combustion cannot escape - pressure increases; the reaction zone is narrowed; heat flow into the explosive increases; the explosive burns faster. Within a few milliseconds the process become self-propagating. To represent this in numbers, the linear burn rate of pine wood at atmospheric pressure is in the order of 0.02 mms-1. Similarly, the linear burn rate of an unconfined gun propellant under the same conditions is typically 5 mms-1. However, if this same propellant is then confined in the breech mechanism of an artillery piece then the linear burn rate can increase to 400 mms-1.
Ultimately, the rate of deflagration in explosives can reach a situation where the rate of burning approaches and exceeds the velocity of sound for that material under the current conditions. If the rate of deflagration reaches values in excess of 1000 – 1800 ms-1 then the reaction is classed as a ‘low order’ detonation.
The propagation of an explosion reaction through a deflagrating explosive is based on thermal reactions. A deflagrating explosive will ignite when subjected to an external stimulus such as flame, spark, shock, friction or high temperatures. Burning begins on or just above its surface, essentially receding layer by layer as one would imagine when sucking a hard boiled sweet. The rate at which the surface of the explosive burns is known as the linear burning rate, which is governed by Equation 1, where r is the linear burning rate coefficient in mms-1, P is the pressure at the surface of the explosive at a given instant in Nmm-2,  is the burning rate coefficient and  is the burning rate index.
𝑟= 𝛽𝑃^∝
Equation 1: Linear Burning Rate
In a deflagration reaction, the temperature of each layer of the explosive is brought to the ignition point as it recedes, with heat being radiated and conducted from the reaction zone into the solid material. The rate at which the surface recedes depends on the rate of heat transfer into the explosive, which itself is dependent upon the pressure at the surface of the composition as Equation 1 demonstrates. As such, the rate of surface regression can increase hugely if the explosive is confined (completely enclosed), since the gaseous products of combustion cannot escape - pressure increases; the reaction zone is narrowed; heat flow into the explosive increases; the explosive burns faster. Within a few milliseconds the process become self-propagating. To represent this in numbers, the linear burn rate of pine wood at atmospheric pressure is in the order of 0.02 mms-1. Similarly, the linear burn rate of an unconfined gun propellant under the same conditions is typically 5 mms-1. However, if this same propellant is then confined in the breech mechanism of an artillery piece then the linear burn rate can increase to 400 mms-1.
Ultimately, the rate of deflagration in explosives can reach a situation where the rate of burning approaches and exceeds the velocity of sound for that material under the current conditions. If the rate of deflagration reaches values in excess of 1000 – 1800 ms-1 then the reaction is classed as a ‘low order’ detonation.

## Slide 9: A deflagration in slow motion
https://www.youtube.com/watch?v=-aXW1TFg_EA

## Slide 10: What is detonation
A detonation is defined as an extremely fast explosive decomposition, in which an exothermic reaction wave maintains a shock front in the explosive material.
Notes: The velocity of that shock front can be in the region of 1800 – 9000 ms-1, dependent upon the explosive. Unlike a deflagration, the rate at which the material decomposes is NOT governed by the rate of heat transfer but by the velocity at which the explosive material will propagate the shockwave. Detonation can take place via two specific mechanisms:
Burning to detonation;
Shock to detonation.
The rapid and violent form of combustion called detonation differs from other forms in that all the important energy transfer is by mass flow in strong compression waves, with negligible contributions from other processes (such as heat conduction) which are so important in flames. The leading part of a detonation front is a strong shock wave propagating into the explosive. This shock heats the material by com­pressing it, thus triggering chemical reactions, and a balance is attained such that the chemical reaction supports the shock wave propagation. In this process material is consumed much faster than in a flame, making detonation easily distinguishable from other combustion processes. The very rapid energy conversion in explosives is the property that makes them useful. The most easily measured characteristic property of a detonation is the velocity at which the front propagates into the explosive. The front of a detonation wave initiated at one end of a large-diameter stick of explosive is found to approach a nearly plane shape and a constant velocity of propagation. Thus, it seems reasonable to assume that a limiting velocity exists, and within that limit a chemical reaction takes place which produces a steady propagating zone in the explosive.

## Slide 11: Transition to detonation
Explosive in advance of the combustion zone can become compressed by thermal expansion. A pressure wave propagates through the unburned material.
Reaction
zone
Shock
zone
Unreacted explosive
The material is now detonating.
This wave can increase in intensity until it is capable of initiating the explosive in advance of the combustion front. It may be travelling at the speed of sound in the material.
Detonation Wave Video

## Slide 12: Charge Diameter and DDT

## Slide 13: Density and DDT
80/20 TRITONAL

## Slide 14: A fortunate deflagration

## Slide 15: A detonation wave in slow motion

## Slide 16: How Does Detonation Occur?
Hot-Spot Formation
  Where energy is concentrated in excess of the ignition temperature/threshold – linking/quenching.
  Cracks, voids, impurities etc as small as 0.1-10𝜇m
  Time duration - 10𝜇s to 1ms
  1. Bubble collapse
  2. Friction
  3. Shear band formation
  4. Crystal fracture
  5. Visco-plastic work
  6. Electrical discharge
Notes: Those hot-spots which are in proximity to one another link together possibly as a result of pressure pulses travelling between the hot-spots as a result of the production of product gases. Hot-spots which are more widely spaced tend to be quenched.

## Slide 17: Primary Explosive – Hot Spots
Ignition for the majority* of primary explosives is via inter-crystalline friction or adiabatic heating, which generate hotspots to overcome activation energy. [*ESD/flame/direct heating]
If the energy created by the hot spots exceeds the activation energy of the primary explosive then deflagration/detonation will proceed with the formation of explosive products and a release of energy.
If not, the hot spots will gradually die out, with no reaction occurring.

## Slide 18: Secondary Explosive – Hot Spots
Ignition for the majority of secondary explosives is through the adiabatic compression of small gas spaces between crystals.
If the heat energy created by the hot spots exceeds the ignition temperature of the explosive, then deflagration/detonation will proceed with the formation of explosive products and a release of energy.
If heat can dissipate then the hot spot gradually dies out, with no reaction occurring.

## Slide 19: Cumbrian Pie Video

## Slide 20: Burning to Detonation
Self-propagating deflagrations are intrinsically unstable and tend to accelerate continuously. Under appropriate conditions, a deflagration will accelerate to a high supersonic velocity and then undergo an abrupt transition to a detonation wave.
Burning to detonation occurs when the pressure at the burning surface accelerates the flame front beyond the velocity of sound of the explosive material under its current conditions. This would be akin to an aircraft exceeding the speed of sound in air, the point at which the sonic boom is heard.
So, we progress from a deflagration to a detonation, suggesting that there will be a delay to the onset. The delay to onset of detonation is dependent upon the nature of the explosive, charge density and conditions of confinement.

## Slide 21: Case Study – the Beirut port explosion
https://forensic-architecture.org/investigation/beirut-port-explosion
12 minutes

## Slide 22: Shock to detonation
In a shock to detonation (or direct initiation) there is no requirement to precede with a flame front through a burning process. Instead, a high velocity shock wave generated by the ignition source is responsible for the detonation formation process.
Notes: In a shock to detonation (or direct initiation) there is no requirement to precede with a flame front through a burning process. Instead, a high velocity shock wave generated by the ignition source is responsible for the detonation formation process. As the shock wave travels into the explosive, particle compression and adiabatic heating occurs at the shock front. Adiabatic heating and compression liberate energy as the explosive decomposes, thereby accelerating the shock wave further. At some point (or not) the velocity of the shock wave will exceed the velocity of sound in the explosive material and detonation will occur. Obviously, the shock wave will be required to travel a distance along the explosive (mm or cm even) before it becomes self-propagating, but unlike a burn to detonation, the delay is in microseconds. If the conditions are not met, again for which there are many variables such as initial shock velocity, charge diameter and loading density, a detonation may not occur, leaving the explosive chemically unchanged. So, in terms of OME there can be many occurrences where explosive charges:
high order (where the conditions to sustain the velocity of the required shock wave are met);
low order (where the explosive is consumed but the shock front is unable to achieve its peak velocity leading to a less violent explosion);
partial (where the shock wave is only able to sustain the appropriate detonation velocity through part of the explosive, leaving part of it chemically unchanged and still visible at the explosion site).

## Slide 23: Energy, Sensitiveness and Power
Energy balance from reaction in an exothermic chemical system
Notes: If sufficient energy is accumulated in a molecule by collision, absorption of light/gamma rays/ cosmic rays, impact by high-speed particles etc. then it is possible that a bond can break. In many cases it is likely that the separated entities produced by the bond breakage recombine almost immediately. However, in some cases the separated entities form strong bonds with other atoms and molecules in the vicinity or undergo further fragmentation. This forms the basis of chemical kinetics. Most chemical reactions start with an endothermic step, this means that energy has to be added to the molecule causing the initial bond breakage., Immediately after separation, the fragments are in a very high energy state. The fragments can lose energy by collision, the particles will lose a lot more energy by forming new bonds or by rearranging and fragmenting further. The energy released by this to other molecules can cause those molecules to fragment and so lead to a succession of chemical reactions. Reactions which give out energy are called exothermic and it is the balance between the endothermic and the exothermic reactions which determines the overall energy output. Figure gives a schematic of the energy release for an exothermic reaction.
The easiest way to concentrate energy into a molecule is by heating it. If once, chemical reaction has started, sufficient energy is released this can cause the system to be self-heating. Effectively a positive feedback mechanism, building up the energy release rate to the phenomenal levels seen in explosives.
The energy required to take a molecule from its normal, standard temperature and pressure (298 K and 1 atmosphere) to the state where its weakest bond breaks is called the activation energy (Eact). The energy difference between the initial material and the final products is the energy that is available for doing other work. In most explosives this means a conversion from a solid or a liquid to a hot, high pressure gas which violently pushes against, fracturing and moving the surrounding material. Figure gives a schematic idea of the energy thresholds and energy output.

## Slide 24: Deflagration to Detonation Transition
If the explosive is sufficiently energetic, and if the heat of combustion is not lost to the environment, the rate of propagation may accelerate, and the pressure wave in advance of the combustion zone may increase in intensity.
In some cases, the pressure may rise sufficiently to cause reaction in advance of the thermal stimulus, and acceleration of the rate occurs.
If the propagation rate increases to the speed of sound in the material, the process is now a detonation – the fastest process that can be achieved in that system.
DDT – deflagration to detonation transition.

## Slide 25: Energy Balance for Explosive ‘X’
Primary explosives are most often used to initiate reactions whereby their chemistry produces a shock wave (or burn rate) of sufficient magnitude to deflagrate/detonate a less sensitive explosive. Ignition for the majority of primary explosives is via inter-crystalline friction, which generates hotspots to overcome activation energy. Hot Spot Ignition Mechanisms for Explosives. John E. Field. Acc. Chem. Res. 15th April 1992, 25, 489 – 496.
Ignition of secondary explosives is primarily through the adiabatic compression of small gas spaces between crystals.

## Slide 26: So, what’s this all about? A Typical Shell
Cap:- Ingniferous input,
percussion or electric,
Lead styphnate based
Additives :-
Graphite in the electric cap.
Lead Oxide
Calcium silicide
Barium Nitrate
Tetrazine in the percussion cap
First Fire layer (or layers)
Usefully fine gunpowder
Either pressed onto the cap or
in magazine in the primer
or both.
Gunpowder G20 in
the primer body. Vents
Through holes and lights
Propellant.
Granular propellant:-
double base, 7 hole granule.
With de-coppering agent
RDX/TNT/Wax filling
Booster pellet:-
Formerly CE (tetryl)
Now RX 3601 or similar
LDNR Stab sensitive
Detonator
Boron based delay.
Switch in / out
In line / out of line
Stemming and
detonator
Booster
LDNR = Lead dinitro resorcinate

## Slide 27: Propelling Charge Components
CONVENTIONAL ARTILLERY CHARGE SYSTEM - “subtractive” increments
INC 2
INC 1
INC 3
CHARGE 1
IGNITER
CONTAINER
INC
INC
INC
INC
INC
MODULAR CHARGE SYSTEM – “additive” increments
Note - in example shown, each increment contains a central igniter

## Slide 28: Charge Components – Artillery & Armour
COMBUSTIBLE CASE
END CAP
STICK PROPELLANT
IGNITER
PAD
Separate
loading
round
Primer
Fixed
Round
PRIMER
CARTRIDGE CASE
GRANULAR PROPELLANT
WEAR LINER

## Slide 29: Propulsion– Igniter Components
Typical example
4.5” Naval
INTERNAL TO CHARGE
EXTERNAL TO CHARGE
Typical example
UK 120mm tank gun
VENT HOLE
Mouth
Closure
SEAL
LINING
CAP
SECONDARY
IGNITION
MAIN
FILLING
BODY
Charge Components

## Slide 30
Fuze
Booster Pellet:- Pressed Rowanex 3601
Shell Body
Flexible Liner
Driving Band & Obturator
Base Bleed Grain
Igniter
Aluminium / Steel Liner
CAST ROWANEX 1100 Filling
155mm L15 HE IM (Extended Range)
Projectiles - Shell Components

## Slide 31: Detonators
Detonators will not necessarily be a container full of lead azide.
They will be assembled in up to four layers.
  Essentially Match, Paper, Wood, Coal.
Construction will depend upon required initiation stimulus and output.
  Electrical, Stab, Flash etc

## Slide 32: Primary Explosives

## Slide 33: A list of primary explosives

## Slide 34: Lead Salts
Lead Azide
Lead Styphnate

## Slide 35: Detonator Schematic / Stab Sensitive (LZY)
Varnish
L-Mixture (32 mg)
Al Cup with turn over
Washer
Tin Antimony Disk
Lead Azide (91 mg)
Tetryl (23 mg)
Code | Description
L LDNR Tetrazole Barium Nitrate | L Mixture 50% 5% 45%
R | 2,4,LDNR (RD 1337)
W | Silver Azide (RD 1336)
Y | Tetryl
Z | Lead Azide (RD 1343)
LAT | Lead Azotetraole (RD 1355)
RDX | RDX (RD 1347)
Notes: Lead Dinitro Resourcinate (LDNR)

## Slide 36: ASA Compositions - igniferous
ASA = lead azide, lead styphnate and aluminium

## Slide 37: OME Performance Requirements
Simplistically, the required effects fall into the following general categories.
High Explosive.
The energy within the explosive material (single chemical or mixture) is released very rapidly. Time scale ~µs
Propulsive.
The rate depends on the requirement.
Gun shell propulsion : ~ s
Rocket propulsion : ~s – long time
Pyrotechnic.
Huge range of requirements : -
Flash/bang (ms)
Combustion delay (~s)
Smoke production (mins), etc..

## Slide 38: OME Performance Requirements
The energy must be released on, and only on demand.
The performance must remain constant under defined storage conditions, for at least the defined lifetime (years).
The munition must remain safe against accidental functioning due to impact, excessively hot storage, etc., etc..
The energetic material should not emit harmful gases on storage.
The energetic material should not produce environmentally unacceptable products on functioning.

## Slide 39: Degradation and Safety
Changes that may occur during the life of a munition include :
Decomposition, or other chemical reaction, of an energetic ingredient leading to increased sensitiveness of the material (increased hazard) or decreased sensitivity (reduced reliability of functioning).
Chemical reaction between an energetic material and non-explosive components of the munition to form explosive compounds where there should be none.
A physical change in the energetic material such as cracking (usually after impact or thermal cycling), or migration of eutectic mixtures (during hot storage).

## Slide 40: Combustion Propagation Rate
Propagation requires transfer of heat from the combustion zone into the unburned energetic material which is usually a solid single ingredient, or a mixture of ingredients perhaps of widely differing physical properties (crystalline solid, solid organic, waxy plasticiser, ….. Etc.)
Heat is also lost from the combustion zone by conduction into the container, by volatilisation of hot reaction products, and perhaps by melting or vaporisation of unreacted or partly reacted energetic material.

## Slide 41: Combustion Propagation Rate
The chemical and physical characteristics of the explosive should therefore be required to remain constant during the life of the munition.
Thermal conductivity and porosity of a material are affected by :
  Density
  Physical structure (cracks, pores, phase change)
Heat can be transferred from the reaction zone into the reactant by thermal conduction and by permeation of hot combustion products into the material.
The environmental conditions to which a particular munition may be subjected, and the total permissible duration, are defined.

## Slide 42: Reaction Rates
Combustion:
  slow (<~400 mm s-1)
  little pressure change through reaction zone
Detonation:
  fast (>~2000 m s-1)
  discontinuous pressure rise through reaction zone (shock wave)

## Slide 43: Detonation
Unit of pressure : Pascal Pa 1N m-2.
Atmospheric pressure (sea level) 101.3 kPa
Car Tyre 260kPa
1000 m below sea level 10.15 MPa
HE detonation pressure >10 GPa

## Slide 44: Detonation Explained
40 kg IED (Human in the open)
Death 100% - 10 m
  Wind speed – 500 mph
Death 50% - 15 m
  Wind speed – 294 mph
Life changing injury - 27 m
  Wind speed – 102 mph
Light injuries – 62 m
  Wind speed – 38 mph

## Slide 45: Explosive Munitions
The required effects include :
Blast – generation of large quantity of hot gas which expands rapidly (initially supersonically) in air to produce a shock wave with shattering effect, and high speed gas flow to move objects.
Fragmentation – rapid expansion of a metallic casing with consequent fracturing and production of high velocity fragments.
Rapid acceleration of a fragment in a specific direction (directed energy) – Shaped Charge, EFP, HESH
Kinetic Energy (sub-hydrodynamic, hydrodynamic) – Long Rod

## Slide 46
Warhead design and selection
Warhead design starts with a target assessment, which should identify the make-up of the target, its strengths and it weaknesses (SWOT analysis!):

## Slide 47
Blast

## Slide 49
Fragmentation
Naturally fragmenting warhead – seldom used in GW warheads but used extensively in artillery and infantry / common user
Controlled fragmenting warheads – fragment shape and size controlled. Sub-groups are discrete fragments (discrete/continuous rod) and ‘fire-formed’ fragmentation systems used to encourage case break-up

## Slide 50
These warheads focus the explosive energy in a given direction to achieve penetration of the target. They are mainly concerned with the attack of well protected targets such as armour. These groups include:
  Shaped charges (SC)
  Explosively formed projectiles (EFPs)
  High explosive squash heads (HESH)
Directed Explosive Energy

## Slide 51: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
ANTI-ARMOUR

## Slide 52: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment

## Slide 53: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
Blast - External
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment

## Slide 54: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
Blast - External
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - Internal

## Slide 55: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
Blast - External
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - Internal

## Slide 56: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
Blast - External
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - Internal

## Slide 57: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
Blast - External
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - Internal

## Slide 58: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-STRUCTURE
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
HESH

## Slide 59: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
HESH
ANTI-STRUCTURE

## Slide 60: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
HESH
ANTI-STRUCTURE

## Slide 61: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
HESH
ANTI-STRUCTURE

## Slide 62: Target Defeat Mechanisms
ANTI-PERSONNEL
ANTI-ARMOUR
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
HESH
ANTI-STRUCTURE

## Slide 63: Target Defeat Mechanisms
ANTI-ARMOUR
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
HESH
Blast - External
Blast - Internal
ANTI-STRUCTURE
SHAPED
CHARGE

## Slide 64: Target Defeat Mechanisms
ANTI-ARMOUR
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
HESH
Blast - External
Blast - Internal
ANTI-STRUCTURE
SHAPED
CHARGE

## Slide 65: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
HESH
Blast - External
Blast - Internal
ANTI-STRUCTURE
SHAPED
CHARGE
ANTI-ARMOUR

## Slide 66: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
HESH
Blast - External
Blast - Internal
ANTI-STRUCTURE
SHAPED
CHARGE
ANTI-ARMOUR

## Slide 67: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
HESH
Blast - External
Blast - Internal
ANTI-STRUCTURE
SHAPED
CHARGE
ANTI-ARMOUR

## Slide 68: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE

## Slide 69: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE

## Slide 70: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE

## Slide 71: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE

## Slide 72: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE

## Slide 73: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 74: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 75: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 76: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 77: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 78: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 79: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 80: Target Defeat Mechanisms
ANTI-PERSONNEL
Blast - HE
KE - bullet
shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
SHAPED
CHARGE
KE
Tandem Warhead

## Slide 81: Target Defeat Mechanisms - Summary
ANTI-PERSONNEL
Blast - HE
KE - shell fragment
Blast - External
Blast - Internal
ANTI-STRUCTURE
ANTI-ARMOUR
HESH
Shaped Charge - HEAT
Tandem Warhead
KE - bullet
KE - APFSDS

## Slide 82: Main Charge Secondary Explosive
High
Detonation
Pressure
Blast
HESH
Fragmentation
Enhanced Blast
High Impulse
Anti-
Vehicle
Anti-
Personnel
Anti-
Vehicle
Performance Requirements
Suppression
Anti-structure
Anti-Structure

## Slide 83: Outline Structure of Munition
lead azide
Examples :
RDX/wax
RDX/TNT
RDX/TNT/aluminium
RDX/polyurethane
tetryl
lead styphnate
Primary
Explosive
Secondary Explosives

## Slide 84: HE Munition
155mm L15
43 kg, 11.4 kg HE
Main Filling
RDX/TNT/wax
melt/cast
Booster
RDX/wax
pressed
Detonator
lead azide

## Slide 85: Primary Explosives
Pb++
-
-
lead azide
Precipitated by the reaction of aqueous solutions of sodium azide and lead nitrate.

## Slide 86: Lead azide
Lead azide I
Lead azide II
Prepared by mixing equal volumes of 1M lead nitrate and 2M sodium azide.
Polymorphic form stable at room temperature.
water
NaN3 solution
Pb(NO3) solution
Pb(N3)2 ppt.
Prepared by slow diffusion of lead and azide ions. Slowly transforms to type I.
Anal. Chem. 28 1791-1793 (1956)

## Slide 87: Primary Explosives
.H2O
resorcinol
2-nitroresorcinol
2,4-dinitroresorcinol
2,4,6-trinitroresorcinol
lead 2-nitroresorcinol (LMNR)
lead 2,4-ditroresorcinol (LDNR)
lead styphnate
HNO3

## Slide 88: Booster Explosives
N,2,4,6-tetranitro-N-methylaniline
Tetryl
mp 131°C
bp explodes 180°C
Tetryl, a yellow waxy solid, was the main booster explosive until ~1970s, but no longer used because of its toxicity (threshold limit for airborne contaminant 1.5 mg.m-3).

## Slide 89: Booster Explosives
RDX is a high melting crystalline solid which is too sensitive to press into pellets.
It is blended with small quantities of various waxy or plastic polymers which can be safely pressed into pellets which are sufficiently sensitive to be detonated by an small amount of primary explosive, and sufficiently powerful to initiate a relatively insensitive secondary explosive.
The pellets are mechanically robust and can readily be assembled into munitions.

## Slide 90: RDX and RDX/Wax 95/5
RDX pure, uncoated
Focal Plane Screening Images
RDX coated with 5% Wax 8
(Debrix 3)
95/5

## Slide 91: RDX/Wax 8 88/12
RDX/Wax 8 8/12
RDX/Wax 8 8/12
lightly crushed
large agglomerates of coated RDX
exposed RDX
Focal Plane Screening Images

## Slide 92: Main Charge Explosives
A main charge explosive must :
Be sufficiently powerful to produce the required effect.
Be sufficiently sensitive to achieve detonation from a booster, but sufficiently insensitive to survive even accidental handling without event.
Undergo no reactions with other components of the munition.
Have mechanical properties sufficient to allow it to be filled at high density into the munition (or a component) by a method suitable for industrial production.
Undergo no significant change in uniformity of composition, density or explosive properties during the design life of the munition.

## Slide 93: 2-4-6-TNT
Melting point 80.9°C (after laboratory purification). Industrial material probably ~80.6°C?
Can readily be filled by melt-casting (vapour is toxic).
Forms eutectics with impurities (largely lower nitration compounds) which can migrate through a filling and exude at an open surface.
  2-4-6-TNT = melting point 80oC, 4-NT = 56oC, 3-NT = 16oC, 2-NT = -10oC
The set point (easier to determine than the melting point) is specified to limit the impurity content.
Readily forms large crystals on solidification, so somewhat brittle, may crack.

## Slide 94: TNT
Solidification process.
On cooling, molten TNT forms long crystals.
When cast into, say, an artillery shell the crystals nucleate at the cooler edge and grow towards the centre.
Their planes of weakness line up, and cracks propagate.

## Slide 95: Cast TNT
HE Shell RDX/TNT

## Slide 96: TNT Recrystallized with HNS
TNT crystals
Sites of nucleation by TNT/HNS complex

## Slide 97: TNT - HNS

## Slide 98: Main Charge Explosives
RDX
Melting point 204°C. Increasingly rapid decomposition on further heating.
Cannot be consolidated into single charge by pressing, so cannot be used alone for munition filling.
Forms a castable slurry with TNT that was the most frequently used filling for many years.
Mixtures with waxes (e.g. RDX/wax 8 88/12) can be pressed into large pellets or into suitable shaped warheads.
Forms castable and extrudable slurries with a range of polymeric materials.

## Slide 99: RDX/Wax/aluminium 70/30
Focal Plane Screening Images
RDX/wax
Al/wax
Brixal 70/30

## Slide 100: Fuel Air Explosives

## Slide 101
Comparison of shock waves
in air and water
Notes: In air, which is a medium of low density and high compressibility the primary shock wave is comparatively short-lived. It decays rapidly due to energy lost by irreversible heating of the air. As the hot, high pressure gaseous products expand immediately behind the primary shock wave that deposited heat energy is captured and contributes to the energy undertaking work compressing the surrounding air, which produces the blast wave. Thus beyond a few charge diameters from the explosion centre there is only one pressure wave to be considered. In water the transmission of shock wave energy is much more efficient because water is some 800 times more dense than air and its compressibility is correspondingly much less. Even so, at the very high shock pressures initially produced on detonation, some energy is lost by inelastic compression of the water.
This efficient transmission of the shock wave allows it to detach and travel away from the expanding gases. When a spherical charge of high explosive, centrally initiated, detonates at moderate depth in deep water, the corresponding spherical shock front travels radially through the charge and into the surrounding water. The water at the interface with the explosive is violently compressed and accelerated. The shock wave thus formed is propagated through the water at up to 5000 m s-1, becoming totally separated from the gas bubble which is expanding relatively slowly behind it. The velocity then decreases quickly to the sonic velocity in water of about 1500 m s-1.
The shock pressure within the explosive charge may be more than 250 kbar but the acoustic impedance mismatch at the interface of the detonation products and the water causes a rarefaction wave to be reflected back into the detonation sphere. Because of this the initial shock wave pressure is approximately one half of the detonation pressure, say 125kbar. The difference between shock pressures in air and water from identical explosive charges is shown above.
Under reasonably good conditions an observer above the water surface can see the manifestation of these separate effects. The primary shock wave from the detonating charge can be seen fleetingly as a rapidly expanding ring of apparently darkened water, often called the 'slick'. This ring is caused by the reflected shock wave pressure momentarily flattening ripples on the surface. Directly above the explosion point, if it is not too deep, a dome of spray appears due to spalling of the water surface as the primary shock wave is reflected. Finally comes the plume of water thrown up by the gas bubble venting at the surface. The shape and size of the plume varies with the depth of the explosion, and a charge at great depth does not create one. These observations will be difficult to separate if the explosion takes place in shallow water.

## Slide 102
FAE Pressure-Time Curve
Notes: The full heat of explosion of a fuel is only realised when it is mixed with its chemical equivalent (stoichiometric) quantity of air. However, a fuel/air explosion is very inefficient in terms of energy (little more than 40%). This is because energy is absorbed by nitrogen in the air, which dilutes the system, and imparting motion to the explosion gases reduces the energy available to the blast wave. The nine-fold advantage of propane over TNT is therefore reduced to four-fold in reality. The initial detonation pressures and velocities in fuel-air explosions are much less than those for an equivalent weight of conventional explosive. Therefore, fuel-air explosions have little comparable brisance or shattering effect. Notwithstanding this, they do have other advantages in the propagation of the air blast.
As we have seen from The profile of a blast wave (diagrammatic), a condensed explosive detonates as a ‘point source’ and the blast overpressure falls rapidly with increasing distance from the charge. In contrast, a fuel-air explosion is a large cloud, which cannot be regarded as a point source and therefore the decay in peak overpressure falls much less rapidly with distance from the edge of the cloud. Furthermore, the duration of the positive phase of the blast wave is greater than that from condensed explosive so the impulse will be even greater. FAE therefore possess the potential to do more work on the surrounding environment, the positive phase duration being an important parameter in the response of structures to a blast. Although on first sight the lower overpressure to that of a conventional solid explosive would seem to be a disadvantage, civilian accidents, trials and operational use have proved the effectiveness of FAE against personnel, soft skinned vehicles, parked aircraft and structures – a maximum overpressure of 0.9 bar is all that is required to sink a ship and this value was obtained from the sinking of the ‘mothballed’ destroyer USS McNulty in 1973 with ethylene and propylene oxide.
The maximum rate of deflagration within a fuel-air cloud, and hence its effectiveness in creating a blast wave, varies for different fuels since the volume occupied by the fuel-air cloud is much greater than a conventional explosive and fluid dynamics are associated with the fuel mixing with the air. Shelkin and Troshin report that 1000 kg of TNT occupies a hemisphere of 0.5 m radius whilst 1000 kg of methane would require a 24m radius. As such, Hopkinson’s scaling law does not apply. Gasodynamics of Combustion

## Slide 103: Recap (press picture!)

## Slide 104: Summary
Mechanism of energy release
combustion, deflagration, detonation; deflagration to detonation transition (DDT)
OME performance requirements – changes during life of munition.
Types of explosive – primary, secondary, tertiary, and … fuel-air.

## Slide 105: Questions