## Slide 1
Electrical Engineering
(ACDA5001)
Lecture - 5

## Slide 2: Content
Pure Resistive circuit
Pure Inductive Circuit
Pure Capacitive Circuit
RL Series Circuit
RC series Circuit
RLC series Circuit

## Slide 3: Learning Outcome
The student upon completion of the lecture will be able to:
Demonstrate the ability to design circuits using Resistor, capacitor and inductor

## Slide 4: Single Phase AC Circuits
Instantaneous Power (p):
The amount of power in a circuit at any instant of time is called instantaneous power. It varies over time.
Average Power (
Average power is the power delivered on average over a complete cycle of an AC waveform. It refers to the real power and represents the usable power in the circuit.
Notes: ▭(" " 𝑝(𝑡)=𝑣(𝑡)" " 𝑖(𝑡)" " )
▭(𝑃_"avg" =1/𝑇 ∫128_(𝑡_0)^(𝑡_0+𝑇)▒𝑣 (𝑡)" " 𝑖(𝑡)" " 𝑑𝑡)
Sinusoidal AC:
𝑃_"avg" =𝑉_"rms" 𝐼_"rms" cos⁡𝜙
This is the real (active) power.
Non-sinusoidal: still 𝑃_"avg" =1/𝑇 " ⁣" ∫128▒𝑣 𝑖" " 𝑑𝑡; equivalently
𝑃_"avg" =𝑉_"rms" 𝐼_"rms" ×"(true PF)"

## Slide 5: Single Phase AC Circuits
Impedance (Z)
Impedance is the total opposition that a circuit offers to the flow of alternating current (AC). It includes both resistance (R) and reactance (X)
Reactance (X)
Reactance is the opposition of change of flow of current within a circuit
Reactance accounts for the opposition to AC due to inductance and capacitance.

## Slide 6: Single Phase AC Circuits
Three Parameters in AC circuits are
Resistance
Inductance
Capacitance

## Slide 7: Pure Resistive circuit
The circuit containing only a pure resistance of and a power supply is known as Pure Resistive Circuit.
The Voltage across the circuit is given as
The Current across the circuit is given as
Applying Ohm’s law
Peak Current,

## Slide 8: Pure Resistive circuit
Peak Voltage
Phase,
Voltage and Current are in phase with each other. Phasor represents the RMS value of the alternating quantities
Phasor Diagram
V
I
Waveform

## Slide 9: Pure Resistive circuit
Instantaneous power
×
If,
Average Power
Watts
Notes: Real power P=𝑽𝑰 𝑪𝒐𝒔∅

## Slide 10: Pure Resistive circuit
Power factor
Impedance
Instantaneous Current
Instantaneous Voltage

## Slide 11: Pure Inductance circuit
The circuit containing only a pure Inductance of L Henry and a power supply is known as Pure Inductive Circuit.
The Voltage through the inductor is given as
The Current through the inductor is given as
Peak Current,

## Slide 12: Pure Inductance circuit
Peak Voltage:
Phase,
Current lags the voltage by . Negative sign represents the lagging nature of the current. Phasor represents the RMS value of the alternating quantities
Notes: In phasor terms: 𝑍_𝐿=𝑗𝑋_𝐿has angle +90^∘; with voltage as reference, 𝐼is at −90^∘.

## Slide 13: Pure Inductance circuit
Phasor Diagram
Waveform

## Slide 14: Pure Inductance circuit
Instantaneous power is
×
If,
Average Power
Notes: sin(ωt−90∘)=−cos(ωt).)
𝑠𝑖𝑛𝜔𝑡.𝑐𝑜𝑠𝜔𝑡 = 1/2 "sin2(ωt")
when the voltage is at its maximum, the current is zero, and vice versa.
There is no net consumption of energy in the inductor over a full cycle. The energy simply oscillates back and forth between the inductor and the source.

## Slide 15: Pure Inductance circuit
Power factor
Impedance
Instantaneous Current
Instantaneous Voltage

## Slide 16: Pure Capacitance circuit
The circuit containing only a pure Capacitance of C Farad and a power supply is known as Pure Capacitive Circuit.

## Slide 17: Pure Capacitance circuit
The Voltage across the circuit is given as
The Current across the circuit is given as
I
Notes: 𝑖=𝑑𝑞/𝑑𝑡
Capacitive impedance:
‾𝑍_𝐶=1/𝑗𝜔𝐶=−" " 𝑗𝑋_𝐶, 𝑋_𝐶=1/𝜔𝐶.
Current from voltage:
‾𝐼_𝐶=‾𝑉/‾𝑍_𝐶 =‾𝑉/(−𝑗𝑋_𝐶 )=(𝑗" " ‾𝑉)/𝑋_𝐶 =𝑗" " 𝜔𝐶" " ‾𝑉.
The factor 𝑗means the current leads the voltage by 90^∘.

## Slide 18: Pure Capacitance circuit
Peak Current,
Peak Voltage:
Phase,
Current leads the voltage by . Positive sign represents the leading nature of the current. Phasor represents the RMS value of the alternating quantities

## Slide 19: Pure Capacitance circuit
Phasor Diagram
Wave Form

## Slide 20: Pure Capacitance circuit
Instantaneous power is
×
If,
Average Power

## Slide 21: Pure Capacitance circuit
Power factor
Impedance

## Slide 22: Pure Capacitance circuit
Instantaneous Current
Instantaneous Voltage

## Slide 23: AC circuits
RMS Current (
RMS Voltage (
Peak Current or Maximum Current ()
.
Peak Voltage or Maximum Voltage
.

## Slide 24: RL series circuits
In RL series Circuit, the Resistor and Capacitor are connected in series across a voltage source as shown in the circuit. The voltage across the Resistor is and the voltage across the inductor is The overall impedance of the circuit is Z.

## Slide 25: RL series circuits
The impedance in RL Circuit is
The Voltage across the circuit is given as
The Current across the circuit is given as

## Slide 26: RL series circuits
Phasor Diagram
The resistor voltage is in phase with the current
The Inductor Voltage (is leading currentby
The resultant voltage is at an angle with the current.
Voltage Triangle
Notes: sin⁡𝜃="opp" /"hyp" , cos⁡𝜃="adj" /"hyp" , tan⁡𝜃="opp" /"adj" =sin⁡𝜃/cos⁡𝜃

## Slide 27
Waveform
Phase()
=
RL series circuits

## Slide 28
Average Power:
Watt
Power factor
RL series circuits
Notes: Real power P=𝑽𝑰 𝑪𝒐𝒔∅

## Slide 29
Total Voltage
Voltage
Phase Angle
Voltage drop across inductor
RL series circuits
Notes: sin⁡𝜃="opp" /"hyp" , cos⁡𝜃="adj" /"hyp" , tan⁡𝜃="opp" /"adj" =sin⁡𝜃/cos⁡𝜃

## Slide 30: RL series circuits
Impedance plot
Real part along X axis,
Imaginary plot along Y axis
Notes: sin⁡𝜃="opp" /"hyp" , cos⁡𝜃="adj" /"hyp" , tan⁡𝜃="opp" /"adj" =sin⁡𝜃/cos⁡𝜃

## Slide 31: RC series circuits
In RC series Circuit, the Resistor and Inductor are connected in series across a voltage source as shown in the circuit. The voltage across the Resistor is and the voltage across the Capacitor is The overall impedance of the circuit is Z.

## Slide 32: RC series circuits
The impedance in RC Circuit is
The Voltage across the circuit is given as
The Current across the circuit is given as
Notes: Capacitor impedance:
𝑍_𝐶=1/𝑗𝜔𝐶=−" " 𝑗 1/𝜔𝐶=−" " 𝑗𝑋_𝐶
because 1/𝑗=−𝑗and 𝑋_𝐶=1/𝜔𝐶.

## Slide 33: RC series circuits
Phasor Diagram
The resistor voltage is in phase with the current
The Capacitor Voltage (lags currentby , Current leads the capacitor voltage ( by
The resultant voltage is at an angle with the current.
Notes: sin⁡𝜃="opp" /"hyp" , cos⁡𝜃="adj" /"hyp" , tan⁡𝜃="opp" /"adj" =sin⁡𝜃/cos⁡𝜃

## Slide 34
Waveform
Phase()
=
RC series circuits

## Slide 35
Average Power:
Watt
Power factor
Voltage Drop across a capacitor
Phase angle
RC series circuits
Notes: sin⁡𝜃="opp" /"hyp" , cos⁡𝜃="adj" /"hyp" , tan⁡𝜃="opp" /"adj" =sin⁡𝜃/cos⁡𝜃

## Slide 36: RC series circuits
Impedance plot
Real part along X axis,
Imaginary plot along Y axis
Notes: sin⁡𝜃="opp" /"hyp" , cos⁡𝜃="adj" /"hyp" , tan⁡𝜃="opp" /"adj" =sin⁡𝜃/cos⁡𝜃
:
▭(cos⁡𝜙=𝑅/(∣𝑍∣)), ▭(sin⁡𝜙=−𝑋_𝐶/(∣𝑍∣)), ▭(tan⁡𝜙=−𝑋_𝐶/𝑅=−𝑉_𝐶/𝑉_𝑅 )

## Slide 37: RLC Series circuit
In an AC series circuit containing Resistance , Inductanceand Capacitance , the applied voltage is the phasor sum of , and .
and are anti-phase, i.e. displaced by
Voltage across the resistor
Voltage across the Inductor
Voltage across the Capacitor

## Slide 38: RLC Series circuit
When,
Impedance,
Phase angle,
Voltage,

## Slide 39: RLC Series circuit
When,
Impedance,
Phase Angle,
)
Voltage,

## Slide 40: RLC Series circuit
Phasor Diagram
When,

## Slide 41: RLC Series circuit
Phasor Diagram
When,

## Slide 42: RLC Series circuit
Phasor Diagram
When,

## Slide 43: RLC Series circuit
Average Power:
Watt
Power factor

## Slide 44: RLC series circuit
When, , the applied voltage and the current are in phase. This effect is called series resonance.
At series Resonance,
(the minimum circuit impedance possible in an L–C–R circuit)
(i.e. the maximum current possible in an L–C–R circuit)
,
Notes: Reactive voltages: ∣𝑉_𝐿∣=∣𝑉_𝐶∣and they are 180° out of phase (phasors cancel), so the net reactive voltage is zero even though each can be large.

## Slide 45: RLC series circuits
Impedance plot
Real part along X axis,
Imaginary plot along Y axis

## Slide 46
References:
[1] J. W. Nilsson and S. A. Riedel, Electric Circuits, 12th ed. Upper Saddle River, NJ: Pearson, 2019.
[2] J. Bird, Electrical Circuit Theory and Technology, 7th ed. London: Routledge, 2021.

## Slide 47: Thank You